## Slide 1
Road Fill
Dirt Gravel and Low Volume Road Program
Remote Training
If you are reading this, then you are successfully seeing the webinar video. Webinar audio should be automatic through your computer (or click “join audio”), and options can be accessed in the “audio options” button on the bottom left. If your computer audio is not working, you can listen on your phone by dialing 312-626-6799.
5/20/2021 Starts at 9am
Audio via Phone if needed: 312-626-6799
Webinar ID: 998 9453 7275
Eric Nevel- CDGRS
Steve Bloser - CDGRS
www.dirtandgravelroads.org

## Slide 2
Purpose:
  Review an expanded version (compared to ESM training) of road fill with additional examples.
  Review available “Request for Quote” for road fill
Filling Road Cross-Section
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 3
Road Fill
  Background
  Filling the Road Profile
  Other Considerations
  Types of Fill
  Introduction to RFQ
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 4: Natural Landscape
SUBSURFACE DRAINAGE PATTERNS
SUBSURFACE DRAINAGE PATTERNS
Surface drainage patterns
Sub-surface drainage patterns
Introduction
How Roads Affect the Land
Notes: The effects of increased erosion are many, but the biggest are increased maintenance problems, as well as excess sediment and chemical runoff to the streams.

## Slide 5: Roads Intercept Natural Drainage
Surface drainage patterns
Sub-surface drainage patterns
Introduction
How Roads Affect the Land
Notes: The effects of increased erosion are many, but the biggest are increased maintenance problems, as well as excess sediment and chemical runoff to the streams.

## Slide 6: Roads Intercept Natural Drainage
Surface drainage patterns
Sub-surface drainage patterns
Notes: The effects of increased erosion are many, but the biggest are increased maintenance problems, as well as excess sediment and chemical runoff to the streams.

## Slide 7
Avoid Concentrating Drainage
Minimize Flow Volumes
Reduce Effects of Concentrated Drainage
Prevent Surface Erosion
Reduce Cost and Frequency of Road Maintenance
ESMP
These are the goals of ALL of the practices in the DGLVR Program
Notes: ALL ESMPs have these five goals
These five principles are the goals of ALL of the Environmentally Sensitive Maintenance Practices we will discuss in the next two days.

## Slide 8
Drainage Disconnection and infiltration are the goals of the DGLVR Program
Road Fill
Hallmarks of the DGLVR program
Keeping sediment & excess runoff out of the stream
Getting water into the ground

## Slide 9
2018 DnG 1/1
Centre County, Yeager Hollow Road
$35K Grant
Summary:
Frequently flooded and soft section of road
Large French Mattress and road fill
AFTER
BEFORE
DURING
DURING
DURING

## Slide 10
AFTER
BEFORE
2018 DnG 1/1
Wayne County, Adams Pond Road
$92K Grants, $17K In-kind
Summary:
Mile long site with poor base
9 New shallow crosspipes installed, ditches reshaped and stabilized
Base improvement and DSA
AFTER
BEFORE

## Slide 11
DURING
2018 DnG 1/1
Bradford County, Jung Road
$92K Grants, $15K In-kind
Summary:
Severely entrenched saturated road
~9,000 tons fill added to achieve sheet flow
1,300 feet of underdrain, new pipes, ditch stabilization
AFTER
BEFORE
DURING

## Slide 12
Environmentally Sensitive Maintenance for Dirt & Gravel Roads
Road Base

## Slide 13
The most important part of a building is the part you can’t see. Roads are the same.
Road Base: Introduction
https://soilsmatter.wordpress.com/

## Slide 14
Road Base: Introduction
It’s impossible to properly maintain the road surface if underlying problems are the cause.
Surface irregularities will hold water, which will further degrade the surface and base and swallow tons of expensive aggregate.

## Slide 15
Ideal Unpaved Road Cross Section
Road Base: Introduction
Subgrade: native earth
Sub-base: larger support rock
Base: free-draining base (2A, etc)
Surface: dense and compact
(often does not exist)

## Slide 16: Ideal Paved Road Cross Section
(Subgrade)
Road Base: Introduction

## Slide 17
Geology
Soils
Soil Moisture
Freeze-thaw
Traffic Loads
Road Base: Introduction
Geology

## Slide 18
18
what do you have to work with?
Road Base: Introduction
Geology

## Slide 19
Glacial Soils
Physiographic Provinces
Road Base: Introduction
Geology
Glacial Soil Issues
- Water/frost susceptibility
- High clay/silt content
- Rounded gravel (lacks angularity)
Glacial Soils

## Slide 20
Glacial Soil Issues
- Water/frost susceptibility
- High clay/silt content
- Rounded gravel (lacks angularity)
Road Base: Introduction
Geology

## Slide 21
Geology
Soils
Soil Moisture
Freeze-thaw
Traffic Loads
Road Base: Introduction
Soils

## Slide 22
TOPSOIL
Highly variable in depth
Home for plants and animals
Full of nutrients and organic matter
Makes a bad road
SUBSOIL
Little organic matter or nutrients
Little growth potential
Road Base: Introduction
Soils

## Slide 23
23
TOPSOIL
SUB-SOIL
Road Base: Introduction
Soils

## Slide 24
Soils are a mixture of :
Sand
Silt
Clay
Road Base: Introduction
Soils
Sand - Large
Silt - Small
Clay – Extremely small and FLAT!!!

## Slide 25
Geology
Soils
Soil Moisture
Freeze-thaw
Traffic Loads
Road Base: Introduction
Soil Moisture

## Slide 26
How does
water move
underground?
Road Base: Introduction
Soil Moisture

## Slide 27
VIDEO
Infiltration Schematic
0:53
Road Base: Introduction
Soil Moisture

## Slide 28
28

## Slide 29
Road Base: Introduction
Soil Moisture
Cracks in rock will channel subsurface water

## Slide 30
Water runs downhill, right?
What about water underground?
Primary movement is downhill by gravity.
BUT……
Underground water can move sideways, and even UP!
Road Base: Introduction
Soil Moisture

## Slide 31
31
How can water enter your road?
Water Table
Through Permeable Surface
Capillary Rise
Seepage from High Ground
Lateral Flow from Roadside
Water Table
Road Base: Introduction
Soil Moisture

## Slide 32
How can water enter your road?
CAPILLARY RISE: Movement of water due to the forces of adhesion, cohesion, and surface tension
Road Base: Introduction
Soil Moisture

## Slide 33: Height of Capillary Rise
Soil Type Height of rise (ft)
Small Gravel < 0.4
Coarse Sand 0.5-1
Fine Sand 1-3
Silt 3-30
Clay 30-90
Road Base: Introduction
Soil Moisture

## Slide 34
Geology
Soils
Soil Moisture
Freeze-thaw
Traffic Loads
Road Base: Introduction
Freeze-Thaw

## Slide 35
FROST DAMAGE:
FREEZE/THAW
EXCESS WATER
FROST HEAVE
Why is there so much water in the spring?
Why do my fence posts rise every winter?
Why do large rocks rise up into my road?
Why does frost damage my road so much?
FROST
HEAVE
Road Base: Introduction
Freeze-Thaw
Notes: I changed the slide to reduce words and highlight the concepts in the upcoming videos

## Slide 36
Three Conditions Causing Frost Heave
Freezing Temperatures
Frost Susceptible Soil
Water Road Bed
Lets talk about FROST
Road Base: Introduction
Freeze-Thaw

## Slide 37: The effect of frost on your roads
Frost Table
Water Table
Road
Snow
COLD AIR
COLD AIR
COLD AIR
Frost Heave
Ice Lenses
Road Base: Introduction
Freeze-Thaw

## Slide 38: The effect of frost on your roads
Frost Table
Water Table
Road
Snow
WARM AIR
WARM AIR
WARM AIR
Ice Lenses
Road Base: Introduction
Freeze-Thaw

## Slide 39
Geology
Soils
Soil Moisture
Freeze-thaw
Traffic Loads
Road Base: Introduction
Traffic Loads

## Slide 40
Road Base: Introduction
Traffic Loads
Traditionally we IGNORE Base Problems
Costs too much
Don’t understand the problem
Perceived as too big of a deal

## Slide 41
Base: Traditional Practices
Traditional “fix” is just to throw rock at the soft spots.
Spending money on symptoms, not fixing the problem
Road has “no bottom”

## Slide 42
Road Fill
  Background
  Filling the Road Profile
  Other Considerations
  Types of Fill
  Introduction to RFQ
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 43
Filling Road Cross-Section
Road Base: ESMPs
Entrenched Roads
Lower than surrounding ground on both sides
Make it impossible to get water off the road
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 44
Filling Road Cross-Section
Road Base: ESMPs
Why are so many of our roads ENTRENCHED?
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 45
Filling Road Cross-Section
Road Base: ESMPs
A 100-year-old road that looses 1/2 inch of material that is not replaced each year will be entrenched 4’ today.
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 46
When:
  Where banks are higher on both sides of the road (entrenched roads)
  When you want to improve base stability
  When you want to shift the road up-slope
  When you want to add road width
Filling Road Cross-Section
Road Base: ESMPs
Page 52 in Field Guide
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 47
SUB-SOIL
ROADWAY
TOP-SOIL
IDEAL CROSS-SECTION
How: Where banks are higher on both sides of the road
Filling Road Cross-Section
Road Base: ESMPs
Page 52 in Field Guide
Notes: Entrenched – Both Banks Higher – Water Trapped
An entrenched road is where both banks are higher than the road, and water on the road and ditches can’t escape.

## Slide 48
SUB-SOIL
ROADWAY
TOP-SOIL
ELIMINATED BANK
REDUCED BANK HEIGHT
FILL
Filling Road Cross-Section
Road Base: ESMPs
Page 52 in Field Guide
Notes: Fill To Eliminate Downslope Bank and Ditch – Can Sheet Flow ½ Road, and Create More Outlet Options For Pipes – Place To Put Snow
By filling the road high enough to eliminate the downslope bank and ditch, water can sheet flow off the downslope side, and pipes from the upslope ditch can be outletted without a high maintenance tail ditch. In addition, you now have some place to put the snow when you plow.

## Slide 49
Filling Road Cross-Section
Road Base: ESMPs
Whenever possible or necessary we should strive to elevate the road surface by building an embankment
Often called “turnpiking”
Fill the hole, build a foundation, and elevate the road surface
Notes: Fill To Eliminate Downslope Bank and Ditch – Can Sheet Flow ½ Road, and Create More Outlet Options For Pipes – Place To Put Snow
By filling the road high enough to eliminate the downslope bank and ditch, water can sheet flow off the downslope side, and pipes from the upslope ditch can be outletted without a high maintenance tail ditch. In addition, you now have some place to put the snow when you plow.

## Slide 50
Filling Road Cross-Section
Road Base: ESMPs
Whenever possible or necessary we should strive to elevate the road surface by building an embankment
Often called “turnpiking”
surat-thani-thailand-oct-25-260nw-1095967559
http://www.envicom.eu/en/portfolio-posts/sizing-and-calculation-of-a-supporting-structure-necessary-to-ensure-stability-of-an-embankment-road-infrastructure-2/
Notes: Fill To Eliminate Downslope Bank and Ditch – Can Sheet Flow ½ Road, and Create More Outlet Options For Pipes – Place To Put Snow
By filling the road high enough to eliminate the downslope bank and ditch, water can sheet flow off the downslope side, and pipes from the upslope ditch can be outletted without a high maintenance tail ditch. In addition, you now have some place to put the snow when you plow.

## Slide 51
Filling Road Cross-Section
Road Base: ESMPs
Whenever possible or necessary we should strive to elevate the road surface by building an embankment
Often called “turnpiking”
surat-thani-thailand-oct-25-260nw-1095967559
Notes: Fill To Eliminate Downslope Bank and Ditch – Can Sheet Flow ½ Road, and Create More Outlet Options For Pipes – Place To Put Snow
By filling the road high enough to eliminate the downslope bank and ditch, water can sheet flow off the downslope side, and pipes from the upslope ditch can be outletted without a high maintenance tail ditch. In addition, you now have some place to put the snow when you plow.

## Slide 52
Figures not drawn to scale.
100
102
ditch
flow
Filling Road Cross-Section
Ditch Outlets ESMPs
ditch
flow
104
106
108
110
Entrenched Road

## Slide 53
Figures not drawn to scale.
100
102
ditch
flow
Filling Road Cross-Section
Ditch Outlets ESMPs
ditch
flow
104
106
108
110
Road
Fill
Entrenched Road
Complete Fill

## Slide 54
Figures not drawn to scale.
100
102
ditch
flow
Filling Road Cross-Section
Ditch Outlets ESMPs
ditch
flow
104
106
108
110
Road
Fill
New pipes
Sheet flow
Entrenched Road
Complete Fill

## Slide 55
What to do?
Long ditch run
Ditch erosion
Ditch blows out stream
Unstable banks
Can’t get pipes or turnouts in
Filling Road Cross-Section
Road Base: ESMPs
1400’ LONG ENTRENCHED ROAD
Example 1: Huntingdon County
Huntingdon County – Red Rose Road – 1/9
BEFORE
Notes: Red Rose Project – Entrenched – Filled Profile and Compared to Rip-Rap
This is Red Rose Road in Huntingdon County, a classic entrenched dirt road in Pennsylvania. The far end of this Road is fairly steep with deep eroded trenches. The Center thought the best fix here was to raise the road to the top of the banks. However, we wanted to compare the cost of raising the road to the cost of the traditional practice of rip-rapping the ditches with properly sized stone.

## Slide 56
BEFORE
IDEAL
ELEVATION
Filling Road Cross-Section
Road Base: ESMPs
Huntingdon County – Red Rose Road – 3/9
Notes: Red Rose Project – Entrenched – Filled Profile and Compared to Rip-Rap
This is Red Rose Road in Huntingdon County, a classic entrenched dirt road in Pennsylvania. The far end of this Road is fairly steep with deep eroded trenches. The Center thought the best fix here was to raise the road to the top of the banks. However, we wanted to compare the cost of raising the road to the cost of the traditional practice of rip-rapping the ditches with properly sized stone.

## Slide 57
Fill and Compact
Ideal
Elevation
Filling Road Cross-Section
Road Base: ESMPs
Huntingdon County – Red Rose Road – 4/9
Notes: Bid Project – Paid Contractor – Free Shale
We bid the job and got a price from a local contractor to fill the road, using material from an adjacent borrow area.

## Slide 58
Huntingdon County – Red Rose Road (4 of 5)
Fill and Compact
Filling Road Cross-Section
Road Banks: ESMPs
Huntingdon County – Red Rose Road – 6/9
Ideal Elevation Achieved
Notes: Finished Subgrade – Notice Crown – Road Can Sheet Flow – No Long Ditch Runs
Here is the finished subgrade. Notice we have built the proper crown into the subgrade before aggregate is placed. Now, the road is wider and can sheet flow off one side. The need for long ditch runs was also eliminated.

## Slide 59
PLACING AGGREGATE
No ditch!
2002
Filling Road Cross-Section
Road Base: ESMPs
Huntingdon County – Red Rose Road – 7/9
New pipe outlet
Notes: DSA Placed Next Year
A year later the DSA was applied to finish the project.

## Slide 60
No ditch!
Filling Road Cross-Section
Road Base: ESMPs
Huntingdon County – Red Rose Road – 8/9
2020
2001
long term improvement!
pipes
Notes: DSA Placed Next Year
A year later the DSA was applied to finish the project.

## Slide 61
Red Rose Road – Huntingdon County - 2020
Road Fill
Entrenched for over 1500 feet, few outlets availabe
Good road base

## Slide 62
Red Rose Road – Huntingdon County
Road Fill
8 cross-pipes (7 new!)
Over 4100 tons of total fill material (shale and 2A)
Shale Fill (average of 1 foot of fill over 3000 feet of road)
Paver placed 2A for surface (6” loose lift)
DSA to be placed (final phase in 2-phase project)

## Slide 63
Red Rose Road – Huntingdon County
Road Fill
Before
After
No concentrated flow

## Slide 64
Red Rose Road – Huntingdon County
Road Fill
Local shale was placed and compacted to promote sheet flow and ditch outlet opportunities

## Slide 65
Red Rose Road – Huntingdon County
Road Fill
Shale has been placed and compacted

## Slide 66
Red Rose Road – Huntingdon County
Road Fill
Downslope driveway accounted for:
Tie in (smooth transition)
Drainage
  Sheet flow established on downslope ditch
  New crosspipe outlets water below the driveway intersecion

## Slide 67
Red Rose Road – Huntingdon County
Road Fill
Shallow cross-pipes were installed in the compacted shale before the 2A surface was placed.

## Slide 68
Red Rose Road – Huntingdon County
Road Fill
Outlet of new cross-pipe at downslope driveway

## Slide 69
Orwell Road – Bradford County
Road Fill

## Slide 70
Orwell Road – Bradford County
Road Fill

## Slide 71
Orwell Road – Bradford County
Road Fill

## Slide 72
Robinson – Bradford County
Road Fill

## Slide 73
Filling Road Cross-Section
Road Base: ESMPs
Jefferson County
AFTER
BEFORE

## Slide 74
Filling Road Cross-Section
Road Base: ESMPs
BOF Dist 6, Cambria Cty – Stevenson Farm Road – 1/6
BEFORE
Cambria County
Entrenchment doesn’t have to be deep to be a problem
Notes: The effects of increased erosion are many, but the biggest are increased maintenance problems, as well as excess sediment and chemical runoff to the streams.

## Slide 75
Filling Road Cross-Section
Road Base: EMSPs
Placing Fill
BOF Dist 6, Cambria Cty – Stevenson Farm Road – 2/6
Notes: The effects of increased erosion are many, but the biggest are increased maintenance problems, as well as excess sediment and chemical runoff to the streams.

## Slide 76
Filling Road Cross-Section
Road Base: ESMPs
BOF Dist 6, Cambria Cty – Stevenson Farm Road – 3/6
Fill and Compact
Compact fill in lifts of 1’ or less
Notes: The effects of increased erosion are many, but the biggest are increased maintenance problems, as well as excess sediment and chemical runoff to the streams.

## Slide 77
Filling Road Cross-Section
Road Base: ESMPs
BOF Dist 6, Cambria Cty – Stevenson Farm Road – 5/6
AFTER
Notes: The effects of increased erosion are many, but the biggest are increased maintenance problems, as well as excess sediment and chemical runoff to the streams.

## Slide 78
Filling Road Cross-Section
Road Base: ESMPs
BOF Dist 6, Cambria Cty – Stevenson Farm Road – 6/6
AFTER
BEFORE
Fill allows for crosspipe
more pipes
Notes: The effects of increased erosion are many, but the biggest are increased maintenance problems, as well as excess sediment and chemical runoff to the streams.

## Slide 79
BEFORE 1
DURING
BEFORE
‘16 LVR Project - Complete
Venango County, Keister Rd
$144K Spent, $31K in kind
Massive fill job, underdrain and DSA
Crosspipes and through the bank pipes
AFTER

## Slide 80
2017: DnG
Potter County, Cobb Hill Road
$75K Grant, $57K In-Kind
Summary:
Poor base and drainage: only 1 crosspipe total in a mile of road.
6,000+ tons of fill, 12 new pipes, 740’ underdrain, off ROW work
BEFORE
Roadway WILL FLOOD: Large mattress provides base support and pipes allow water to drain in both directions
AFTER
BEFORE
AFTER
Outlet swale through field
New base allowed for multiple new pipes
road = ditch

## Slide 81
BEFORE 1
‘16 D&G Project - Complete
Snyder County, Mattern Rd
$40K Spent, $7K in kind
Driveway pipe and gradebreak
Base improvements
Fill, pipes, and DSA
AFTER
BEFORE
Geotextile and fill
Driveway pipe, grade break and 150’ of DSA

## Slide 82
82
2017 D&G Project
Armstrong County
Gibson School Road
$56K Spent
$56K in kind
Problems:
SEVERELY entrenched road
No drainage outlets
Practices Used:
Road fill and pipe
PROJECT SPOTLIGHT
BEFORE

## Slide 83
2017: D&G Project
Armstrong County, Gibson School Road
$56K Spent, $56K in kind
Summary:
Nearly 10,000 tons of fill
New pipes
BEFORE
SEVERELY entrenched roadway. Drainage improvements were impossible without fill. Entire road drained to headwater stream.
BEFORE

## Slide 84
Township placed 9,800 tons of fill (6,300 tons of soil and shale, 3,500 tons of limestone.
BEFORE
AFTER
Shale fill
Limestone fill
New pipe headwall

## Slide 85
Township placed 9,800 tons of fill (6,300 tons of soil and shale, 3,500 tons of limestone).
BEFORE
AFTER
2017: D&G Project
Armstrong County, Gibson School Road
$56K Spent, $56K in kind
Summary:
Nearly 10,000 tons of fill
New pipes
Worked with landowner to outlet some pipes on other side of hay field in woods.
3 New pipe headwall
Close-up

## Slide 86
BEFORE
AFTER
New pipe headwalls
2017: D&G Project
Armstrong County, Gibson School Rd
$56K Spent, $56K in kind
Summary:
Nearly 10,000 tons of fill
New pipes
Worked with landowner to outlet some pipes on other side of hay field into woods.

## Slide 87
Sectional Fill:
  When you can’t fill the road (either logistics or cost)
  Transition into and out of road fill.
  Short section of fill forces ditch turnout, and provides cover for a new crosspipe.
Filling Road Cross-Section
Road Base: ESMPs
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 88
Figures not drawn to scale.
100
102
ditch
flow
Filling Road Cross-Section
Ditch Outlets ESMPs
ditch
flow
104
106
108
110
Entrenched Road

## Slide 89
Figures not drawn to scale.
100
102
ditch
flow
Filling Road Cross-Section
Ditch Outlets ESMPs
ditch
flow
104
106
108
110
Entrenched Road
sectional Fill
Road
Fill
no fill
no fill

## Slide 90
Filling Road Cross-Section
Road Base: ESMPs
McKean Cty – Prospect Rd – 1/7
Example 3: “sectional FILL” OPTION
BEFORE

## Slide 91
Filling Road Cross-Section
Road Base: ESMPs
McKean Cty – Prospect Rd – 1/7
Example 3: “sectional FILL” OPTION

## Slide 92
Filling Road Cross-Section
Road Base: ESMPs
sectional Fill Option
McKean Cty – Prospect Rd – 2/7
BEFORE

## Slide 93
Filling Road Cross-Section
Road Base: ESMPs
Adding Fill
McKean Cty – Prospect Rd – 3/7
Enough fill used to
build crown
reestablish ditch function
reduce the flow volume reaching stream.
sectional Fill Option

## Slide 94
Filling Road Cross-Section
Road Base: ESMPs
At a select location near the project midpoint enough fill is used to create ditch outlets.
McKean Cty – Prospect Rd – 4/7
sectional Fill Option

## Slide 95
Filling Road Cross-Section
Road Base: ESMPs
A crosspipe and turn-out are installed in the elevated road section.
elevated
still entrenched here
AFTER
McKean Cty – Prospect Rd – 5/7
sectional Fill Option

## Slide 96
Filling Road Cross-Section
Road Base: ESMPs
Elevated road and ditches relieves ditch flow volumes, reduces erosion and road problems.
AFTER
McKean Cty – Prospect Rd – 6/7
elevated
still entrenched here
sectional Fill Option

## Slide 97
Filling Road Cross-Section
Road Base: ESMPs
Elevated road and ditches relieves ditch flow volumes, reduces erosion and road problems.
sectional Fill Option
AFTER
McKean Cty – Prospect Rd – 7/7
elevated
still entrenched here

## Slide 98
BEFORE
AFTER
Susquehanna County
Road Fill Overview

## Slide 99: To costly?
Filling the road is a long-term solution that solves a host of problems
Eliminates ditches and need for rip-rap.
Reduces bank heights and constant resurfacing.
Creates drainage outlets.
Easier to plow snow off the roadway.
Filling Road Cross-Section
Road Base: ESMPs
Notes: Here Are The Numbers - $9,000 or 20% Cheaper Even If Have To Buy Fill
Here’s what the numbers told us. Because the shale was free and available on site, we needed to adjust our figures to reflect the true cost of material and hauling when shale was not free. But even after this adjustment, the cost of filling the road was $9,000, or 20%, cheaper than using rip-rap.

## Slide 100
Challenges of
wider roads:
Maintaining Crown
More re-graveling, grading, plowing, and money $$$
Increased site lines = faster speed
  Faster surface degradation
  More dust
Filling Road Cross-Section
Road Base: ESMPs
Notes: The purpose of effective surface drainage is to keep water off the road, and reduce problems for drivers and maintenance crews alike.

## Slide 101
Wider roads
Must pay
  attention to
  limits of ROW
Consider raising the road, but not over-widening the cartway.
NPDES Permit could apply.
  If there is over 1.0 acre of disturbance outside of existing road “cross-section”
Filling Road Cross-Section
Road Base: ESMPs
Road Fill
Final Road Width
Avoid over-widening the cartway when filling
Road Fill
Notes: The purpose of effective surface drainage is to keep water off the road, and reduce problems for drivers and maintenance crews alike.

## Slide 102
Program has averaged 440,000 tons of fill per year the last 5 years
Filling Road Cross-Section
Road Base: ESMPs
That’s enough material to fill a football field almost 1,000 feet over 5 years.
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 103
Road Fill
  Background
  Filling the Road Profile
  Other Considerations
  Types of Fill
  Introduction to RFQ
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 104
Road Fill
  Other Considerations
    Geosynthetics
    Structural Reinforcement
    French Mattresses
    Underdrains
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 105
Separation FABRIC
Geo-GRID
Notes: Geo-Synthetics Can Be Used For Slope Reinforcement
Geo-synthetics, or “manmade earth”, have multiple applications, including slope reinforcement.

## Slide 106
Separation Fabric: Plastic “cloth” used to separate different materials in soil.
Separation Fabric
Notes: Geo-Synthetics Can Be Used For Slope Reinforcement
Geo-synthetics, or “manmade earth”, have multiple applications, including slope reinforcement.

## Slide 107
Separation Fabric Uses:
Separates two types of material
  Adds some strength
  Distributes loads over larger area
  Prevent clogging of underdrains
No Separation Fabric
Separation Fabric
stone
sand
stone
sand
Separation Fabric
Notes: Geo-Synthetics Can Be Used For Slope Reinforcement
Geo-synthetics, or “manmade earth”, have multiple applications, including slope reinforcement.

## Slide 108
Considerations:
Allows water to pass through
Not biodegradable
Should be buried 1 foot minimum
Many types, sizes, thicknesses, and uses
Some typical rolls: (600 sqyd) - $400
  12.5’ wide x 432’ length
  15’ wide x 360’ length
  17.5’ wide x 309’ length
Separation Fabric
Notes: Geo-Synthetics Can Be Used For Slope Reinforcement
Geo-synthetics, or “manmade earth”, have multiple applications, including slope reinforcement.

## Slide 109
Types:
Two major classifications:
  Woven
    separation
    Support
    4-10 gpm/sqft
  Non-woven
    separation
    filtering
    95-140 gpm/sqft
Separation Fabric
Notes: Geo-Synthetics Can Be Used For Slope Reinforcement
Geo-synthetics, or “manmade earth”, have multiple applications, including slope reinforcement.

## Slide 110
Types:
Recommended uses for each class of fabric:
  Woven
    Base support for road in soft soils
    Deadman anchors in stacked walls
    Erosion control under rock armoring
  Non-Woven
    Sub-surface drainage – Underdrain
    French Mattress
  Consult manufacturer for intended use
Separation Fabric
Notes: Geo-Synthetics Can Be Used For Slope Reinforcement
Geo-synthetics, or “manmade earth”, have multiple applications, including slope reinforcement.

## Slide 111
Separation Fabric
Separation FABRIC
Geo-GRID
Notes: Geo-Synthetics Can Be Used For Slope Reinforcement
Geo-synthetics, or “manmade earth”, have multiple applications, including slope reinforcement.

## Slide 112
GEO-GRID: Plastic grid used to stabilize and strengthen soil.
Geo-Grid
Notes: Geo-Synthetics Can Be Used For Slope Reinforcement
Geo-synthetics, or “manmade earth”, have multiple applications, including slope reinforcement.

## Slide 113
Geo-Grid Uses:
Strengthen road base
Spreads weight (snowshoe effect)
Geo-Grid
Notes: Geo-Synthetics Can Be Used For Slope Reinforcement
Geo-synthetics, or “manmade earth”, have multiple applications, including slope reinforcement.

## Slide 114
Considerations:
Does not separate material like fabric
Adds more strength than fabric
Spreads weight better than fabric
Reduces depth of fill required.
Should be buried 1 foot minimum
Many types, sizes, patterns, and uses
Typical roll: 600 sqyd, $1,500
Geo-Grid
Notes: Geo-Synthetics Can Be Used For Slope Reinforcement
Geo-synthetics, or “manmade earth”, have multiple applications, including slope reinforcement.

## Slide 115
Common Uses Uses will be detailed throughout training
Geo-Grid
Notes: Geo-Synthetics Can Be Used For Slope Reinforcement
Geo-synthetics, or “manmade earth”, have multiple applications, including slope reinforcement.

## Slide 116
Road Fill
  Other Considerations
    Geosynthetics
    Structural Reinforcement
    French Mattresses
    Underdrains
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 117
Structural Reinforcement
Road Base: ESMPs
Structural Reinforcement: Addition of rock and/or geo-synthetics to establish a solid road base
Notes: The purpose of effective surface drainage is to keep water off the road, and reduce problems for drivers and maintenance crews alike.

## Slide 118
Importing new “bridge rock”
  Structural support
  Drainage
Structural Reinforcement
Road Base: ESMPs
Notes: The purpose of effective surface drainage is to keep water off the road, and reduce problems for drivers and maintenance crews alike.

## Slide 119
Separation:
Fabric keeps sub-base and sub-grade separate
(keeps mud below and stone on top)
Imported Base Course
Imported Sub-Base
FABRIC
Geo-reinforced Roads
Road Base: ESMPs
Notes: The purpose of effective surface drainage is to keep water off the road, and reduce problems for drivers and maintenance crews alike.

## Slide 120
Geo-reinforced Roads
Road Base: ESMPs
Low lying LVR
Saturated base soils
Example 1: Huntingdon County
Huntingdon Cty – Miller Rd – 1/9
Notes: The use of Fabric keeps the aggregate separate from the base material, reduces “pumping”, and spreads vehicle weight to minimize rutting.

## Slide 121
Geo-reinforced Roads
Road Base: ESMPs
The “tar and chip” surface and underlying soil was excavated prior to placing fabric
Huntingdon Cty – Miller Rd – 2/9
Notes: The use of Fabric keeps the aggregate separate from the base material, reduces “pumping”, and spreads vehicle weight to minimize rutting.

## Slide 122
Geo-reinforced Roads
Road Base: ESMPs
The bridge rock was tailgated and spread with a loader
Huntingdon Cty – Miller Rd – 4/9
Notes: The use of Fabric keeps the aggregate separate from the base material, reduces “pumping”, and spreads vehicle weight to minimize rutting.

## Slide 123
Geo-reinforced Roads
Road Base: ESMPs
Another layer of fabric was added to keep the surface gravel on the surface.
This is very similar to a French mattress, which we’ll discuss next.
Huntingdon Cty – Miller Rd – 6/9
Notes: The use of Fabric keeps the aggregate separate from the base material, reduces “pumping”, and spreads vehicle weight to minimize rutting.

## Slide 124
Geo-reinforced Roads
Road Base: ESMPs
2RC was tailgated and will be “tarred and chipped”
Huntingdon Cty – Miller Rd – 7/9
Notes: The use of Fabric keeps the aggregate separate from the base material, reduces “pumping”, and spreads vehicle weight to minimize rutting.

## Slide 125
Geo-reinforced Roads
Road Base: ESMPs
Huntingdon Cty – Miller Rd – 8/9
Any water that comes out of the ground under the road surface will now migrate into the ditch instead of saturating the road base
“Bridge Rock”
Notes: The use of Fabric keeps the aggregate separate from the base material, reduces “pumping”, and spreads vehicle weight to minimize rutting.

## Slide 126
Geo-reinforced Roads
Road Base: ESMPs
Huntingdon Cty – Miller Rd – 9/9
One year later
Before
“Bridge Rock”
Notes: The use of Fabric keeps the aggregate separate from the base material, reduces “pumping”, and spreads vehicle weight to minimize rutting.

## Slide 127
Geo-GRID
“snowshoe”
spreads load
strong support
ROUGH GUIDE:
The structural support added by geo-grid typically can produce a 40% reduction in fill height for the same strength.*
*Rule of thumb only: depends on fill material, kind of grid, moisture, etc.
Geo-reinforced Roads
Road Base: ESMPs
Notes: The purpose of effective surface drainage is to keep water off the road, and reduce problems for drivers and maintenance crews alike.

## Slide 128
Geo-reinforced Roads
Road Base: ESMPs
Place Geo-synthetics between sub-grade and base coarse
Imported Base Course
GEO
Sub-grade
Notes: The purpose of effective surface drainage is to keep water off the road, and reduce problems for drivers and maintenance crews alike.

## Slide 129
Geo-GRID
“snowshoe”
spreads load
strong support
Geo-reinforced Roads
Road Base: ESMPs
Notes: The purpose of effective surface drainage is to keep water off the road, and reduce problems for drivers and maintenance crews alike.

## Slide 130
Road Fill
  Other Considerations
    Geosynthetics
    Structural Reinforcement
    French Mattresses
    Underdrains
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 131
French Mattress: A drainage structure under a road consisting of coarse rock wrapped in fabric through which water can freely pass.
Road
STONE
FABRIC
WATER FLOW
French Mattress
Road Base: ESMPs

## Slide 132
When to use a French Mattress
To reconnect wetland hydrology divided by road
Very effective in:
  sloped and lowland wetlands
  areas with wet banks
  areas with saturated road base
  floodplains
Page 17 in Field Guide
French Mattress
Road Base: ESMPs

## Slide 133
When to use a French Mattress
French Mattress
Road Base: ESMPs

## Slide 134
French Mattress
Road Base: ESMPs
A French Mattress is very flexible to fit your site!
short
long
with or without embedded pipes
Road

## Slide 135
French Mattress
Road Base: ESMPs
A French Mattress is very flexible to fit your site!
short
long
with or without embedded pipes

## Slide 136
French Mattress
Road Base: ESMPs
Mattresses are flexible, a few examples: Bedford County
Can use French Mattress to build up road over unstable wetland soils

## Slide 137
French Mattress
Road Base: ESMPs
Mattresses are flexible, a few examples: Centre County
Long mattress with pipes due to wetland and backwatering from lake
Mattress outlets
Note drainage outlet
~200’ mattress used to bridge and drain a “perpetual aggregate-eating mudhole”

## Slide 138
French Mattress
Road Base: ESMPs
Mattresses are flexible, a few examples: Pike County
Long mattress with pipes due to wetland and backwatering from lake

## Slide 139
Important Notes:
Make sure you make it wide enough to build road on top!
French Mattress
Road Base: ESMPs
18” x 20’ mattress
24 feet
20 feet
18 feet
Every situation is different, but you may need a 24’ wide mattress at the base to achieve a 18’ final road width!

## Slide 140
Road Fill
  Other Considerations
    Geosynthetics
    Structural Reinforcement
    French Mattresses
    Underdrains
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 141
Underdrain : A buried drainpipe that collects subsurface water before it surfaces on the road and directs it to a stable outlet.
Underdrains
Road Base ESMPs
Page 12
in Field Guide
Notes: Discussed in “Banks”
We talked about these buried drains in the “Banks” section.

## Slide 142
When TO USE:
Saturated road bases
Perpetually wet ditches and banks
ANY CONSISTENTLY
WET AREAS!
Underdrains
Road Base: ESMPs
Notes: Consider Underdrains When:
Wet Ditches, Banks, Spots in Road
Dry Bank and Remove Lubrication
Consider an Underdrain when you see perpetually wet ditches and banks along the road. They can even be installed under the cartway to dry out problem wet spots. When you dry out wet ditches and drain wet banks, you remove lubrication from the equation and make your banks more stable.

## Slide 143
Underdrains
Road Base: ESMPs
Consider time of year, this is the same site in:
MARCH
MAY
Notes: Cumberland County Project:
Drain Wet Ditch To Far Side
Dave and Dave
Now let’s look at an underdrain project the Center did a couple of years ago in Cumberland County, to drain a wet ditch through the road base and outlet the water to the far side of the road. If you pay attention, you’ll see my two ugly associates in these next slides.

## Slide 144
1. Excavate Trench
2. Place Geo-textile
3. Add pipe and clean fill
4. Add clean fill
5. Wrap and overlap geo-textile
6. Cover geo-textile
FHWA Geosynthetic Design and Construction Guidelines (Berg, et. al., 1998)
Underdrains
Road Base: ESMPs
Constructed Stone Underdrain
Notes: Constructed Underdrain:
Built Any Size – For Any Flow
Clean Filter Stone Also Carries Water
Slide of Steps of Construction
A constructed underdrain can be built to any size, to handle any anticipated flow. The clean stone surrounding the drain pipe will carry water as well. I’ve seen a lot of field drains made only of stone. This slide shows the steps of constructing an underdrain.

## Slide 145
Underdrains
Road Base ESMPs
Jung Road – Bradford County
You can take advantage of deep ditches for underdrains. Much of the excavation is already done for you.
Notes: Discussed in “Banks”
We talked about these buried drains in the “Banks” section.

## Slide 146
Underdrains
Road Base: ESMPs
Example 1
Before
Underdrain excavation

## Slide 147
Underdrains
Road Base: ESMPs
Have a plan to remove excavated material
Should have ~1% slope like a pipe

## Slide 148
Non-Woven Fabric
- separates
filters
Underdrains
Road Base: ESMPs
Page 12 in Field Guide
Placing fabric in trench

## Slide 149
Underdrains
Road Base: ESMPs
Page 12 in Field Guide
Perforated Pipe
Clean Stone
Constructing Underdrain
Notes: Dig to Desired Width and Depth to Allow For Min. 12” Cover
Ensure Minimum 1% Slope
Line With Geo-Fab
Clean Stone Bedding
Lay Pipe
The trench was excavated to the desired width, and deep enough to allow for sufficient cover of the completed underdrain. The backhoe operator made sure their was at least 1% slope, so the drain would drain . The trench was then lined with enough geo-fabric to overlap on top. Clean stone was laid in the bottom as pipe bedding, and the perforated drain pipe was laid on top of the stone.

## Slide 150
Underdrains
Road Base: ESMPs
Page 12 in Field Guide
Underdrain Outlet
Constructing Underdrain
Notes: Dig to Desired Width and Depth to Allow For Min. 12” Cover
Ensure Minimum 1% Slope
Line With Geo-Fab
Clean Stone Bedding
Lay Pipe
The trench was excavated to the desired width, and deep enough to allow for sufficient cover of the completed underdrain. The backhoe operator made sure their was at least 1% slope, so the drain would drain . The trench was then lined with enough geo-fabric to overlap on top. Clean stone was laid in the bottom as pipe bedding, and the perforated drain pipe was laid on top of the stone.

## Slide 151
Underdrains
Road Base: ESMPs
Page 12 in Field Guide
Underdrain Outlet
Constructing Underdrain
Notes: Dig to Desired Width and Depth to Allow For Min. 12” Cover
Ensure Minimum 1% Slope
Line With Geo-Fab
Clean Stone Bedding
Lay Pipe
The trench was excavated to the desired width, and deep enough to allow for sufficient cover of the completed underdrain. The backhoe operator made sure their was at least 1% slope, so the drain would drain . The trench was then lined with enough geo-fabric to overlap on top. Clean stone was laid in the bottom as pipe bedding, and the perforated drain pipe was laid on top of the stone.

## Slide 152
Underdrains
Road Base: ESMPs
Page 12 in Field Guide
Underdrain Notes:
Use clean gravel
AASHTO #1’s work well
“Fist-sized” stone
Notes: Dig to Desired Width and Depth to Allow For Min. 12” Cover
Ensure Minimum 1% Slope
Line With Geo-Fab
Clean Stone Bedding
Lay Pipe
The trench was excavated to the desired width, and deep enough to allow for sufficient cover of the completed underdrain. The backhoe operator made sure their was at least 1% slope, so the drain would drain . The trench was then lined with enough geo-fabric to overlap on top. Clean stone was laid in the bottom as pipe bedding, and the perforated drain pipe was laid on top of the stone.

## Slide 153
Underdrains
Road Base: ESMPs
Non-Woven Fabric
- separates
filters
Underdrain Notes:
Wrap all sides in fabric
Overlap all fabric seems 1’+
Notes: Dig to Desired Width and Depth to Allow For Min. 12” Cover
Ensure Minimum 1% Slope
Line With Geo-Fab
Clean Stone Bedding
Lay Pipe
The trench was excavated to the desired width, and deep enough to allow for sufficient cover of the completed underdrain. The backhoe operator made sure their was at least 1% slope, so the drain would drain . The trench was then lined with enough geo-fabric to overlap on top. Clean stone was laid in the bottom as pipe bedding, and the perforated drain pipe was laid on top of the stone.

## Slide 154
Underdrains
Road Base: ESMPs
Underdrain Notes:
Cover the fabric to hold it in place.
Try to build a ditch shape with the rock used to cover the fabric.
Notes: Dig to Desired Width and Depth to Allow For Min. 12” Cover
Ensure Minimum 1% Slope
Line With Geo-Fab
Clean Stone Bedding
Lay Pipe
The trench was excavated to the desired width, and deep enough to allow for sufficient cover of the completed underdrain. The backhoe operator made sure their was at least 1% slope, so the drain would drain . The trench was then lined with enough geo-fabric to overlap on top. Clean stone was laid in the bottom as pipe bedding, and the perforated drain pipe was laid on top of the stone.

## Slide 155
Underdrains
Road Base: ESMPs
1 year later
Notes: Dig to Desired Width and Depth to Allow For Min. 12” Cover
Ensure Minimum 1% Slope
Line With Geo-Fab
Clean Stone Bedding
Lay Pipe
The trench was excavated to the desired width, and deep enough to allow for sufficient cover of the completed underdrain. The backhoe operator made sure their was at least 1% slope, so the drain would drain . The trench was then lined with enough geo-fabric to overlap on top. Clean stone was laid in the bottom as pipe bedding, and the perforated drain pipe was laid on top of the stone.

## Slide 156
Road Fill
  Background
  Filling the Road Profile
  Other Considerations
  Types of Fill
  Introduction to RFQ
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 157
What is fill?
Road Fill
-Fill is usually aggregate, rock, or subsoil (soil from beneath the topsoil) which has little soil organic matter or biological activity.
-Fill should be as free of organic matter as possible since organic matter will decompose creating pockets of empty space within the fill which could result in settling.
-Uneven or excessive settling of the fill can result in damage to any structures built on the fill.
-Fill is generally required to provide sufficient strength to hold form when compacted or placed.

## Slide 158
Fill
Road Fill
Types of fill include:
- Select Fill
- General Fill
- Non-structural fill
- Rock Fill
- Permeable Fill

## Slide 159
Select Fill
Road Fill
Select fill is superior quality material, used principally as capping, surface material, structural material and/or shoulder material. Select fill materials are commonly specified for use in the construction of:

## Slide 160
Select Fill
Road Fill
Select fill is superior quality material, used principally as capping, surface material, structural material and/or shoulder material. Select fill materials are commonly specified for use in the construction of:
the earthworks layer immediately beneath the pavement layers
spill-through abutment fills and behind abutment areas of bridge approach embankments
reinforced soil embankments
fill placed adjacent to retaining walls
pipe and culvert backfill.

## Slide 161
Select Fill
Road Fill
The maximum stone size for select fill used for roadwork's is 3 inches.
Select fill is required to be compacted; and when compacted, should be non-permeable (i.e water should not flow through it).

## Slide 162
General Fill
Road Fill
General fill is a medium quality material which does not meet the requirements of select fill. General fill materials are usually used to:
Provide a stable platform during construction so that select fill and pavement layers can be satisfactorily placed.
Provide an elevated platform for a pavement such that adequate clearance is provided between the groundwater table or inundation level and the bottom of the pavement, and to protect the pavement from moisture infiltration.
Provide a more economical earthworks design than when using higher quality material for the whole of the fill embankment.

## Slide 163
Non-Structural Fill
Road Fill
Non-structural fill is a lesser quality material which does not meet the requirements of select fill or general fill material, and which may be used in non-structural zones of embankments.

## Slide 164
Rock Fill/Permeable Fill
Road Fill
Rock fill is a permeable material comprised of larger rock and rock fragments which may be used as drainage layers in areas subject to inundation or groundwater inflows or where general and non-structural fills are unsuitable, commonly due to the low strength of in situ soils.

## Slide 165
Road Fill
  Background
  Filling the Road Profile
  Other Considerations
  Types of Fill
  Introduction to RFQ
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 166
Introduction to RFQ
Road Fill
The CDGRS Road Fill Request for quote is very similar to the CDGRS Driving Surface Aggregate Request for quote.
  both are optional
  both are based on overcoming common problems encountered on projects by CDGRS staff and are not meant to be all-inclusive.
  Conservation Districts (CDs) and others can tailor this RFQ to help them obtain quality fill to meet their needs.
  The RFQ can allow for lower costs on deep fill projects by using lower quality fill deep in the profile where frost and abrasion are not an issue.
  Using an RFQ gives the CD the ability to review and accept/reject material.
Since many CD’s already have identified suitable fill material, they would not necessarily need to use the RFQ for that purpose, but an RFQ is a good way to hold a contractor accountable for the quality of fill material.

## Slide 167
Introduction to RFQ
Road Fill
Available online in Word format
You can tailor it to your needs
Has blanks for you to fill in data

## Slide 168
Introduction to RFQ
Road Fill
Available online in Word format
Has optional information or information you choose based on project

## Slide 169
Introduction to RFQ - Material
Road Fill
Section 4 – Road Fill Material
A. Any fill material used must be reviewed and approved by the Road Owner or their designee. This includes quarried materials with specifications. Acceptable and non-acceptable USCS designations are listed below. Any samples shall be obtained by the Owner or their designee (e.g. Conservation District (CD) Staff, Center for Dirt and Gravel Road Studies (CDGRS) staff, or person(s) otherwise approved by the SCC). Road fill material must meet the following minimum requirement
The following USCS soil types are acceptable as both deep and shallow fill materials.
a. GW – well-graded gravel (2A)
b. GM – silty gravel (low clay 2RC, DSA, 2A “modified”)
Shallow fill (select fill) – Material that is buried less and 30 inches below the finished road surface
Deep fill (general fill) – material that is buried greater than 30 inches below the finished road surface
Red text = directly from RFQ

## Slide 170
Unified Soil Classification System (USCS)
Road Fill
The USCS is a soil classification system used in engineering and geology to describe the texture and grain size of a soil or aggregate. The classification system can be applied to most unconsolidated materials and is represented by a two-letter symbol. Each letter is described below (with the exception of Pt)

## Slide 171
Unified Soil Classification System (USCS)
Road Fill

## Slide 172
Introduction to RFQ - Material
Road Fill
Section 4A – Road Fill Material
b. Rock and gravel larger than 3 inches may be used as shallow fill as long it is clean.
Example: AASHTO #1 stone as a road base or in a French Mattress. The void spaces between the rocks keeps them from heaving to the surface.
2. The following USCS soil types (general fill) are acceptable only as deep fill:
      GP – Poorly graded gravel (lacks fines for compaction, good for drainage)
GC – clayey gravel (use only as last resort)
SW – Well graded sand (sand is highly erosive if exposed)
SP – Poorly graded sand (highly erosive)
SM – Silty sand (excellent deep fill material)
SC – Clayey sand (use only as last resort)
ML – Silt (must be low plasticity and adequate density)
CL – Lean clay (must be low plasticity and adequate density),
Or a combination of these groups.
Red text = directly from RFQ

## Slide 173
Additions to RFQ are encouraged
Road Fill
If you are going to use the RFQ, you may want to have an engineer make more specifications to the material, such as:
-Minimum acceptable dry density (proctor test needed)
- Maximum plasticity index
- Maximum liquid limit
- Select fill only
You can make the winning bidder or contractor prove the material meets any specifications by making sampling & testing part of the contract.
Material testing of fill should be a rare event, only needed when an unknown questionable source of fill becomes available, or when there is a history of issues with a particular fill source. Testing allows CDs to reject material in advance of a project (similar to DSA, it is better to identify problems before there are trucks lined up on the project). If testing is required, then Testing Requirements can be inserted into the RFQ in coordination with the Center for Dirt and Gravel Center staff and/or Municipal Engineer.

## Slide 174
Introduction to RFQ - Material
Road Fill
Section 4A – Road Fill Material
3. PennDOT approved quarried aggregates and 4-inch minus are acceptable shallow and deep fill materials
4. Unsatisfactory fill material includes, but is not limited to, the following:
      Unsatisfactory Soils/Aggregates: USCS Classifications per ASTM D 2487*
        OL – Organic silt
        CH – Fat clay (high plasticity)
        MH – Elastic silt
        OH – Organic clay
        Pt – Peat
        Or a combination of these groups

## Slide 175
Introduction to RFQ - Material
Road Fill
Section 4B – Road Fill Material
Excavated Shale is an acceptable material. Shale material must be pre-approved by the Owner or their designee prior to use.
    Shale fill may be used as deep fill, shallow fill and subbase fill if the finished driving surface will be stone aggregate.
    Shale may not be used as the finished driving surface.
      If shale is used for shallow fill then it must be capped with a minimum depth of 6-inches of stone aggregate (e.g. 2A, 2RC, etc.)
      *****Not all shale is created equal!!!!
      - It can contain clay or breakdown once excavated and rained on.
      If you are unsure of the material, at least get someone out to look at it.

## Slide 176
Introduction to RFQ - Material
Road Fill
Section 4B – Road Fill Material
  Fill materials must be clean fill and be uncontaminated, non-water soluble, non-decomposable and inert.
  Fill material shall be free of debris, waste, frozen materials, vegetation, and other deleterious matter.
  This section is for alternative fill materials only. These materials often require extra testing to make sure they will not contaminate the environment. Use this section only if using alternative products such as dredged material, used asphalt, brick, or concrete, slag, bottle glass, foundry sand, coal combustion products, etc.
  For more details, read the entire section in the RFQ…

## Slide 177
Introduction to RFQ - Placement
Road Fill
Section 5 – Delivery and Placement.
  Section I. Geotextile shall be installed on the sections of roads designated by the Owner or their designee.
    Geotextile must be installed over designated deep fill materials listed in Section 4.4, prior to placement of shallow fill.
    Total length of road to receive geotextile is ______ feet. Install geotextile a minimum width of ______ feet.
    Geotextile shall be covered with a minimum of 12 inches (DESIGNATE MIN. DEPTH) of material.
    Install class 2A woven geotextile, or approved equal.
    This section can simply be deleted if no geotextile is used.

## Slide 178
Introduction to RFQ - Placement
Road Fill
Section 5 – Delivery and Placement.
  Section J. Geogrid shall be installed on the sections of roads designated by the Owner or their designee.
    Where required install geogrid on the existing road surface and place fill material over geogrid. Geogrid shall be covered with a minimum of ____ inches of material.
    Total length of road to receive geogrid is ______ feet. Install geogrid a minimum width of ______ feet.
    Install (TYPE OF GEOGRID), or approved equal.
    This section can simply be deleted if no geotextile is used.

## Slide 179
Introduction to RFQ - Placement
Road Fill
Section 5 – Delivery and Placement
Choose section A or B.
Section A. (Turnpiking) Used on fill projects that are going to raise the finished surface above existing grade on both sides of the road/downslope side of road. Specify an average depth on the contract
Section B. Used on partial fill projects. “Install road fill at an average depth of ____ inches to elevate finished driving surface to allow for installation of drainage structures”.
- you may have varying fill heights on your project, be sure they are specified in the work plan and marked on-site if possible.

## Slide 180
Introduction to RFQ - Placement
Road Fill
Section 5 – Delivery and Placement
  Section C. Placement Method
    Road fill is to be placed in 8-inch maximum lifts and compacted with a minimum 10-ton vibratory roller.
    Soft rock materials like shale, sandstone, and cohesive soils like silts and lean clays can be placed in lifts up to 12 inches if a padfoot roller is used for compaction.
https://tuffmanequip.com/product/10-ton-roller
https://constructionor.com/sheepsfoot-rollers/
https://www.cat.com/en_AU/products/new/equipment/compactors/soil-compactors/106520.html

## Slide 181
Introduction to RFQ - Placement
Road Fill
Section 5 – Delivery and Placement.
Section D. Road fill placements should be placed in an even lift the full width of the roadway.
- This allows for complete, even, and consistent compaction and will reduce any future settling of material
- Start thinking about building crown or cross-slope from the very first lift. This may require initial lift(s) that are slightly uneven.
- Deep ditches may need to be filled & compacted before the road can be raised.

## Slide 182
Introduction to RFQ - Placement
Road Fill
Section 5 – Delivery and Placement.
Section E. The crown or cross slope of the roadway after fill placement must range from ½ to ¾ inch per foot (4-6%) for roads that will have a gravel driving surface.
Section F. The crown or cross slope of the roadway after fill placement must range from ¼ to ½ inch per foot (2-4%) for roads that will have a paved driving surface.
- Too often this is not done, and road surface ends up being too flat to drain.
- Putting this in the contract is the only to enforce that it is done. Will most likely require oversight to make it happen.

## Slide 183
Introduction to RFQ - Placement
Road Fill
Section 5 – Delivery and Placement.
Section G. If freezing temperatures or precipitation are forecast that may cause the material to freeze, or prevent the material from drying out, placement may be postponed at the discretion of the road owner, Conservation District, or material supplier.
Section H. Any area(s) which do not meet minimum fill depths, minimum widths, road crown requirements shall be corrected in a manner acceptable to the Owner, at no expense to the Owner.

## Slide 184
Road Fill
  Background
  Filling the Road Profile
  Other Considerations
  Types of Fill
  Introduction to RFQ
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 185
Benefits of Road Fill
Provides cover for drainage
Eliminates downslope ditch
Promotes sheet flow
Improves road base
Reduces bank instabilities
Road Fill
Helps winter maintenance
Improves subsurface drainage
Widens road
LONG TERM solutions to many road issues

## Slide 186
Program has averaged 440,000 tons of fill per year the last 5 years
Filling Road Cross-Section
Road Base: ESMPs
That’s enough material to fill a football field almost 1,000 feet over 5 years.
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 187
Environmentally Sensitive Maintenance for Dirt & Gravel Roads
Questions?
Discussion?
Notes: This Section – Bank Management
In this section we will focus on the management of road banks.