## Slide 1
In-Stream Structures & Grade Control

## Slide 2: Overview….
slope dictates dominant bedforms
  length and spacing of bed features
step / plunge pool
6.1 %
‘pocket-water’
3.2 %
riffle / pool
1.2 %

## Slide 3: Connecting the dots…
Objective is to re-establish channel continuity
  minimize channel adjustment (erosion and sedimentation)
  increase longevity of the new crossing (flood resiliency)
  maintain AOP

## Slide 4: Slope is the key.
Channel Slope
  dictates dominant bedform & grade controls
      refugia / resting zones (pockets and pools) for AOP
  drives bed shear and entrainment
  As channel slope increases…
    channels become less sinuous
    energy dissipation more vertical
    grade control more frequent and robust

## Slide 5: Grade control maintains channel slope and stability.

## Slide 6: Instream structures
Primary functions
  replicate natural instream grade control elements
  keep substrate (streambed) within the culvert
    establish hydraulic control for upstream pool depth
    Define channel cross-section and low-flow channel
  maintain continuity through modified stream reach
Secondary functions
  Streambank protection / erosion control (thalweg maintenance)
    Instream habitat improvement

## Slide 7: Instream rock structures
Rock clusters and cascades
  Mimic natural rock cascade / drop structures
  Size rock for higher-gradient / energy / sediment supply reaches
    Smaller channels and culverts (hand labor)

## Slide 8: Instream rock structures
Rock clusters and cascades
  Can usually re-purpose native, onsite rock
  Minor-frequent grade control
  Built to defined cross-section (width & thalweg)
    Ribs and ‘key pieces’ for constructed riffle

## Slide 9: Instream rock structures
Rock cross vanes
  Mimic natural rock cascade / drop structures
  Suitable for higher-gradient / energy / sediment supply reaches
    Robust grade control

## Slide 10: Instream rock structures
Rock cross vanes…
  Upstream ‘throat’ elevation sets the bed elevation
  Crest-to-crest slope sets channel slope
  Arm angle and slope is important
    Tie arms to bank at or near bankfull elevation and width
    Steeper channel more structures closer together (hydraulic control)

## Slide 11: Instream rock structures
Rock cross vanes…
  Can be constructed inside culvert pipes
  Must be large enough to be stable in flood
    Gapped to allow for AOP

## Slide 12: Instream rock structures
Rock cross vanes…
  Alternating sequence to restore over-widened channels
  Can promote erosion of opposite bank
    Can become undermined in steep channels
US Fish & Wildlife Service

## Slide 13: Instream rock structures
Constructed Riffles
  Relatively-easy to build (easier than it looks!) – especially inside a culvert…
  Relies on ribs and clusters of “key pieces” to hold grade in streambed

## Slide 14: Instream rock structures
Constructed Riffles
  Dominant grade control element in riffle/pool bedform streams
  Suitable for low- to moderate-gradient / energy / sediment supply reaches

## Slide 15: Instream rock structures
Constructed Riffles
  Think energy dissipation – floodplain instead of vertical plunge
  AOP and instream habitat means more than just fish…
  Important to maintain low-flow channel and cross-section shape
  Should not exceed typical bankfull width

## Slide 16: Instream log structures
Single log vanes
  Installed with upstream invert at bed elevation
  Low- to moderate-gradient / energy / sediment supply reaches
    Good for thalweg control

## Slide 17: Instream log structures
Multi-log vanes
  Installed with upstream invert raised above bed elevation
  Low- to moderate-gradient / energy / sediment supply reaches
    Often used for thalweg control & bank protection

## Slide 18: Instream log structures
Log cross vanes
  Similar in function to rock cross vanes
  Best in moderate-gradient / energy / sediment supply reaches
    Promote pool features

## Slide 19: Instream log structures
Log cross vanes
  Can be built with upstream log-framed deflectors
  Arm angle and slope varies by channel slope
    Can withstand undermining better than rock cross vanes

## Slide 20: Log cross vanes as culvert grade control

## Slide 21: Instream log structures
Mud sills
  Primarily bank protection
  Can include log vane “arms” for grade / thalweg control
    Good for reclaiming scour pool width

## Slide 22: Instream log structures
Mud sill – before construction

## Slide 23: Instream log structures
Mud sill – during construction

## Slide 24: Instream log structures
Mud sill - completed

## Slide 25: Instream log structures
Root wads
  Primarily bank protection / habitat improvement
    Good for reclaiming scour pool width
    Can be integrated with other structures

## Slide 26: Instream log structures
Root wads
  Angle upstream and shingle/overlap for scour protection
    Usually require footer and brace logs/rock
    Place so they’re still effective at low-flow

## Slide 27: Questions ?