## Slide 1
Presenters:
Tim Ziegler
PSU Center for Dirt & Gravel Road Studies
Shaun McAdams
PSU Center for Dirt & Gravel Road Studies
Estimating Quantities and Costs
Dirt Gravel and Low Volume Road Program
WEBINAR
2/16/23
Starts 9am
If you are reading this, then you are successfully seeing the webinar video. Webinar audio should be automatic through your computer (or click “join audio”), and options can be accessed in the “audio options” button on the bottom left. If your computer audio is not working, you can listen on your phone by dialing 646-876-9923.

## Slide 2
  Purpose: To share ideas for estimating materials, to generate projected costs for DGLVR projects
  Recommended procedure:
  Determine road plan and the practices included
  Determine needed quantities for each practice
  Itemize and combine quantities for the plan
  We will cover:
  Material quantities for common ESM practices
  Commonly overlooked items
Estimating Quantities & Costs

## Slide 3
Estimating Quantities & Costs
DGLVR Materials Calculator

## Slide 4
Estimating Quantities & Costs
Road Fill/Road Base
Crosspipe/Storm Sewer Installation
Subsurface Drainage
Driving Surface Aggregate
Stream Crossing Replacement
Estimating material quantities for ESM practices:

## Slide 5
Estimating Quantities & Costs
Road Fill/Road Base
Estimating material quantities for ESM practices:

## Slide 6
Estimating Quantities & Costs
Data to collect in the field for road fill estimates
Measure Fill Length at road centerline

## Slide 7
Estimating Quantities & Costs
Measure Fill Width at the top of bank
Data to collect in the field for road fill estimates

## Slide 8
Estimating Quantities & Costs
Measure Fill Depth at road shoulder
Data to collect in the field for road fill estimates

## Slide 9
Estimating Quantities & Costs
Full Fill Option (for sectional fill break into segments)
Estimating material quantities for ESM practices:
Measure on road shoulder
Length x Width x Depth in feet = cubic feet of compacted material required (in place)
Cubic feet ÷ 27 = cubic yards required (in place)
Cubic yards x 1.33 = cubic yards of
uncompacted material required (as shipped)
Cubic yards of uncompacted material x 1.5 =
tonnage of material required (as shipped)

## Slide 10
Estimating Quantities & Costs
Estimating material quantities for ESM practices:
Measure on road shoulder
Example fill calculation
1,400’ long project: 900’ needs 2.5’ of fill and 500’ needs 1’ of fill
Calculate for 2.5’ fill segment:
900’ L x 25’ W x 30”(2.5’) D = 56,250 ft³
56,250 ft³ ÷ 27 = 2,083 yd³ compacted fill
2,083 yd³ x 1.33 = 2,770 yd³ loose fill required
2,770 yd³ x 1.5 = 4155 tons required for 900’
But, there is a simpler way to do this…..

## Slide 11
Estimating Quantities & Costs
Example Road Fill
900’ long
25’ wide
30” deep
shale
$ 9/ton
For the 2.5’ fill stretch

## Slide 12
Estimating Quantities & Costs
Estimating material quantities for ESM practices:
Measure on road shoulder
Example fill calculation
1,400’ long project: 900’ needs 2.5’ of fill and 500’ needs 1’ of fill
Calculate for 1’ fill segment:
500’ L x 25’ W x 12”(1’) D = 12,500 ft³
12,500 ft³ ÷ 27 = 463 yd³ compacted fill
463 yd³ x 1.33 = 616 yd³ loose fill required
616 yd³ x 1.5 = 924 tons required for 500’

## Slide 13
Estimating Quantities & Costs
Example Road Fill
500’ long
25’ wide
12” deep
shale
$ 9/ton
For the 1’ fill stretch

## Slide 14
Estimating Quantities & Costs
Estimating material quantities for ESM practices:
Measure on road shoulder
Example fill calculation
Add together segments for entire project:
900’ at 30”(2.5’) D = 4,167 tons or 2,778 yd³
500’ at 12”(1’) D = 926 tons or 617 yd³
Total fill amount required for project (as shipped):
5,093 tons or 3,395 yd³

## Slide 15
Estimating Quantities & Costs
Good things to know -
Estimating material quantities for ESM practices:
Measure on road shoulder
A tri-axle truck hauls ~14 yd³ or 21 tons of fill
The previous example will require approx. 243 tri-axle truck deliveries to the project site
Shale/bank-run often priced by the truck load (use total yd³ ÷ 14 to figure truck loads)
Don’t discount total fill volume for pipes, French Mattresses, underdrains, etc.

## Slide 16
Estimating Quantities & Costs
Fill for Base Enhancement
Estimating material quantities for ESM practices:
Measure on road shoulder
Calculated the same as Full Fill Option, but…
fill width is the road width, including shoulders, not bank to bank.

## Slide 17
Estimating Quantities & Costs
Road Fill/Road Base
Crosspipe/Storm Sewer Installation
Subsurface Drainage
Driving Surface Aggregate
Stream Crossing Replacement
Estimating material quantities for ESM practices:

## Slide 18
Estimating Quantities & Costs
Crosspipe/Storm Sewer Information
Data to collect in the field for pipe estimates
Measure on road shoulder
Collect Info for:
Length of pipe needed by pipe diameter
Each pipe length can vary by desired inlet and outlet locations (keep lengths to 10’ intervals)
Number of drop inlets/junction boxes needed
Need for and size of outlet protection
If pipes will be shallow or standard installation
- Shallow crosspipes need more fill per pipe

## Slide 19
Estimating Quantities & Costs
Crosspipe/Storm Sewer Pipe Quantity
Estimating material quantities for ESM practices:
Measure on road shoulder
For quantity of pipe:
Take the total length of each diameter pipe needed ÷ 20 = # of sticks for each diameter
For collared pipe, the number of joints = number of collars needed
Consider pipe angle when calculating the length of pipe needed. Round individual pipe lengths to nearest 10’. Half sticks are usable, smaller are not.

## Slide 20
Estimating Quantities & Costs
Crosspipe bedding and cover needs
Estimating material quantities for ESM practices:
Measure on road shoulder
For typical 15” and 18” pipes:
Combine total length of 15” and 18” pipe = total length of trench in feet
Default to 3.5’ width for pipe trench
Use 3’ for trench depth to ensure minimum 12” pipe cover
Total trench length x 3.5 x 3 = the volume of pipe backfill needed (solve for tons as with road fill or use Materials Calculator)…

## Slide 21
Estimating Quantities & Costs
Crosspipe bedding and cover needs
Estimating material quantities for ESM practices:
Measure on road shoulder
Why this wide and deep you ask?
Jumping Jack has 8” wide foot
15” pipe has 19” ID
18” pipe has 22” ID
Crush protection for pipes prior to surfacing

## Slide 22
Estimating Quantities & Costs
Crosspipe bedding and cover needs
Estimating material quantities for ESM practices:
Measure on road shoulder
Do not discount for the volume displaced by the pipe. Any extra fill will help to smooth in trench edges.

## Slide 23
Estimating Quantities & Costs
Crosspipe bedding and cover needs
Estimating material quantities for ESM practices:
Measure on road shoulder
Thumb rule for pipe bedding on standard crosspipes:
Calculate for uncompacted material
240’ of 15” pipe in plan x
3.5’ wide trench x 3’ deep trench = 2,520 ft³ ÷ 27 = 93 yd³ x 1.5 (basic conversion factor) = approx. 140 tons
(approx. 6.5 tri-axle loads)
OR
1/2 tri-axle load of fill for each 20’ stick of 15” or 18” pipe used is close enough for small jobs and government work.

## Slide 24
Estimating Quantities & Costs
Specific to Replacement Crosspipes and Storm Sewer bedding
Estimating material quantities for ESM practices:
Measure on road shoulder
Storm sewers and existing deep pipe installations may require greater fill volumes, depending on depth and municipal regulations.
Take field measurements to accurately account for the fill needs of these structures.
Do not discount for the volume displaced by the pipe.
+++

## Slide 25
Estimating Quantities & Costs
Specific to Shallow Crosspipes with associated grade breaks
Estimating material quantities for ESM practices:
Measure on road shoulder
Shallow pipes gain cover by importing material and raising the road over the pipe.
The actual amount of needed fill will depend on road width and the taper into the road surface in each direction. This should be determined in the field. But a thumb rule of
Two tri-axle loads of aggregate for each shallow crosspipe
works well for estimating.

## Slide 26
Estimating Quantities & Costs
Example Pipe Bedding
40’ long
3.5’ wide
36” deep
2RC
$15/ton
If you like math, you can use your hand calculator. Or…
You can use the Materials Calculator
For small jobs with ≤ 10 pipes, the thumb rule of ½ truckload per 20’ stick will get you close for standard pipe installations

## Slide 27
Estimating Quantities & Costs
Crosspipe/Storm Sewer inlet/outlet protection
Estimating material quantities for ESM practices:
Measure on road shoulder
Headwalls, endwalls, bank walls and scour aprons:

## Slide 28
Estimating Quantities & Costs
Crosspipe/Storm Sewer headwalls/bank walls
Estimating material quantities for ESM practices:
Measure on road shoulder
A typical pallet of wall stone is one cubic yard and weighs 1 ½ tons.
Four typical pipe walls can be built out of each pallet of wall stone.
The rule above is for 15” & 18” crosspipes. Larger drainpipes and stream culverts need more stone.

## Slide 29
Estimating Quantities & Costs
Crosspipe/Storm Sewer precast inlets & outlets
Estimating material quantities for ESM practices:
Measure on road shoulder
If you use drop inlets on crosspipes, you must still account for endwalls.
Figure inlet numbers and any needed junctions.
Note that inlet grates are sold separately.
Headwalls and endwalls constructed of materials other than natural stone (i.e., pre-cast blocks, poured in-place concrete, pre-cast headwalls, etc.) require site specific estimates. Consult local suppliers.

## Slide 30
Estimating Quantities & Costs
Crosspipe/Storm Sewer outlet scour protection
Estimating material quantities for ESM practices:
Measure on road shoulder
The need for scour protection aprons is typically a judgement call based on anticipated flow, soil stability, and steepness at the outlet.
The size of the apron is also a judgement call.
R-4 & R-5 riprap over geofabric is commonly used.
For tons of rip-rap required multiply the apron length x width x depth (1.5’ for R-4 and 2’ for R-5) ÷ 27 to get yd³ x 1.4 = tons to order. Or plug figures into the Materials Calculator…

## Slide 31
Estimating Quantities & Costs
Road Fill/Road Base
Crosspipe/Storm Sewer Installation
Subsurface Drainage
Driving Surface Aggregate
Stream Crossing Replacement
Estimating material quantities for ESM practices:

## Slide 32
Estimating Quantities & Costs
Field data to get for subsurface drainage practices
Measure on road shoulder
Length, width, and depth of the underdrain or French Mattress.
The above is determined by site conditions:
  For underdrain ask what is peak flow anticipated, consider number of outlets and physical site constrictions
  For Mattresses account for desired road width, road elevation, base stability, embedded pipes

## Slide 33
Estimating Quantities & Costs
Underdrain design/estimating considerations
Estimating material quantities for ESM practices:
Measure on road shoulder
Perforated flexible pipe is available in rolls or more rigid sections in different diameters. Estimate required amount by the linear foot.
AASHTO 1 stone recommended for subsurface drainage applications.
Non-woven separation fabric is recommended for subsurface drainage applications.
Separation fabric for constructed underdrain requires a double layer on the top.

## Slide 34
Estimating Quantities & Costs
Underdrain design/estimating considerations
Estimating material quantities for ESM practices:
Measure on road shoulder
Example of underdrain material estimation:
Determine pipe diameter desired and length required
Calculate rock needs per method for crosspipe fill
(disregard the pipe displacement)
Determine geotextile needs by:
Length x 3X Width x 2X Depth = ft² required
(5,400 ft² or 600 yd² per roll)
Factor a minimum of 1’ of cover over underdrain
(R-4 or AASHTO 1 often recommended)
Length’ x 2X the UD Width’ x 1’ ÷ 27 x 1.4 = ~tons

## Slide 35
Estimating Quantities & Costs
Example Underdrain
150’ long
1.5’ wide
18” deep
AASHTO #1
$22/ton

## Slide 36
Estimating Quantities & Costs
French Mattress estimating considerations
Estimating material quantities for ESM practices:
Measure on road shoulder
Example of French Mattress material estimation:
Determine length of mattress (specified linear distance in the road)
Calculate rock needs by:
Length’ x Width’ x Depth’ = ft³ ÷ 27 = yd³ required
X 1.4 = tonnage required
Determine geotextile needs by:
2X Length’ x 2X Width’ (accounts for top and bottom) x 2X Depth’ (accounts for each end) + 2X Length’ if linear overlap is required, and 1X Width’ for each lateral overlap required = ft² required
(*rolls come in 12.5’ x 432’, 15’ x 360’, 17.5 x 308’)
Remember to factor in 1’ of compacted cover over Mattress. Don’t cover inlet/outlet of mattress.

## Slide 37
Estimating Quantities & Costs
Example French Mattress
100’ long
22’ wide
12” deep
AASHTO #1
$22/ton

## Slide 38
Estimating Quantities & Costs
Road Fill/Road Base
Crosspipe/Storm Sewer Installation
Subsurface Drainage
Driving Surface Aggregate
Stream Crossing Replacement
Estimating material quantities for ESM practices:

## Slide 39
Estimating Quantities & Costs
Driving Surface Aggregate
Estimating material quantities for ESM practices:
Measure on road shoulder
DSA estimates are generally calculated on a cost per ton in-place. This figure includes the cost of material, hauling to site, paver placement, compaction, and traffic control.

## Slide 40
Estimating Quantities & Costs
Driving Surface Aggregate
Estimating material quantities for ESM practices:
Measure on road shoulder
DSA Tonnage Estimation
4 ½” compacted lift (6” loose): L’ x W’ x .030 = tons
6” compacted lift (8” loose) use: L’ x W’ x .040 = tons

## Slide 41
Estimating Quantities & Costs
Example DSA
3,500’ long
18’ wide
6” deep (loose)
DSA
$38/ton

## Slide 42
Estimating Quantities & Costs
DSA pre-placement considerations
Estimating material quantities for ESM practices:
Measure on road shoulder
Road base preparation is often overlooked on jobs with DSA placement. The road base must be graded to reflect the finished road shape desired. This may require supplemental road base material to be included in the plan.
Anytime a grant application includes only DSA, further investigation is warranted. Few project sites won’t benefit from drainage, base improvements, and other ESMs prior to DSA paving.
“You’ve got to bake the cake before you can ice it!”

## Slide 43
Estimating Quantities & Costs
Road Fill/Road Base
Crosspipe/Storm Sewer Installation
Subsurface Drainage
Driving Surface Aggregate
Stream Crossing Replacement
Estimating material quantities for ESM practices:

## Slide 44
Estimating Quantities & Costs
Stream Crossing Replacement
Estimating material quantities for ESM practices:
Measure on road shoulder
Comprehensive Projects:
Replacement Structure
  Structure
  Foundation (Bedding)
  Footings (if bottomless)
  Backfill
Instream Restoration
  Streambed material
  Grade Control features
  Bank Margins
  Bank Stabilization
Roadway
  Road base
  Surfacing
  Drainage, etc.

## Slide 45
Estimating Quantities & Costs
Stream Crossing Replacement
Estimating material quantities for ESM practices:
The Site Assessment Tool is your most valuable resource!

## Slide 46
Estimating Quantities & Costs
Stream Crossing Structure
Estimating material quantities for ESM practices:
Measure on road shoulder
First must allow for:
  bankfull channel width
  properly-sized (stable) bank margins
  adequate bury depth
  Q100 / 80% rule.
After these are met:
  cannot be less than 125% bankfull width at bank margin elevation.
Use Site Assessment Tool to predict a suitable structure size
With Your Applicant:
Discuss pros / cons of invert vs. bottomless vs. bridge options
Agree on a preferred structure type and size for the grant application
Slope >4.0% or width >20' is bottomless

## Slide 47
Estimating Quantities & Costs
Stream Crossing Structure
Estimating material quantities for ESM practices:
Measure on road shoulder
Cost estimate
  Use a recent quote – similar type/size
    ($ per linear foot)
  Contact the vendor
    Lane Enterprises
    Contech Engineered Solutions
Full invert structure – only need a quote for the structure (delivered)
Bottomless structure – need a quote for the structure and for footings
  Pre-cast
  Pour-in-place
  Express footer
Contact a local concrete supplier for pricing
Structure vendor or applicant may be able to help

## Slide 48
Estimating Quantities & Costs
Stream Crossing Structure - Footings
Estimating material quantities for ESM practices:
Measure on road shoulder
Use the Site Assessment Tool!
On "Bottomless Recommendations" tab:
  Provides footer height
  Assume a footer width (Width)
  Use Proposed Structure Length (Length)
  Volume = H x W x L

## Slide 49
Estimating Quantities & Costs
Stream Crossing Structure – Foundation / Bedding
Estimating material quantities for ESM practices:
Measure on road shoulder
Typically a 2”-minus stone
  2A Modified, or 2RC (where available)
For a full invert structure
  Width = Structure width + 6’ (3’ on each side)
  Length = Structure length
  Depth = 6” (0.5’)
  Use the materials calculator to determine volume (W x L x D)
For bottomless structure
  Width = 3’ (assumed for base of footing)
  Length = Structure length
  Depth = 8” (0.67’)
  Volume x 2 (two footings)

## Slide 50
Estimating Quantities & Costs
Stream Crossing Structure – Streambed Material
Estimating material quantities for ESM practices:
Measure on road shoulder
How Much Material Do I Need?
  Use the Site Assessment Tool (either of the Recommendations graphs)
  Determine length of reconstructed reach
  If depths vary significantly, break the reconstructed reach into segments (Length)
  Estimate an average depth of fill required for each segment (Depth)
Segment 1
ST 44 to 88 (44’)
~ 0.5’ cut
Segment 2
ST 88 to 130 (42’)
~ 1.0’ fill
Segment 2
ST 130 to 170 (40’)
~ 2.0’ fill

## Slide 51
Estimating Quantities & Costs
Stream Crossing Structure – Streambed Material
Estimating material quantities for ESM practices:
Measure on road shoulder
How Much Material Do I Need?
Assume channel will be reconstructed to the bankfull width (Width)
Use (Length) and average fill (Depth) from each segment
  Remember the Scour Pool cross-section
Use the materials calculator (V = W x L x D)
What Material Do I Need?
Pebble counts give the most reliable basis
Usually a 3-part mix, in equal parts
  Reference Reach
    Largest material size
    Material size moveable at bankfull flow
    Finer materials
May be able to use fines from excavated onsite (“project reach” pebble count)

## Slide 52
Estimating Quantities & Costs
Stream Crossing Structure – Grade Controls
Estimating material quantities for ESM practices:
Measure on road shoulder
What Material Do I Need?
Measure largest grade control rock in reference reach
Use this as a basis for estimating
  Engineer will determine actual size in design
(Length) and (Depth) of rock sill
Depth
Length

## Slide 53
Estimating Quantities & Costs
Stream Crossing Structure – Grade Controls
Estimating material quantities for ESM practices:
Measure on road shoulder
How Much Material Do I Need?
Use the Site Assessment Tool!
  Grade control (Length)
  Assume constructed to bankfull (Width)
(Depth) from largest Grade Control rock in reference reach
Use materials calculator to determine volume for each sill (V = W x L x D)

## Slide 54
Estimating Quantities & Costs
Stream Crossing Structure – Bank Margins
Estimating material quantities for ESM practices:
Measure on road shoulder
How Much Material Do I Need?
Use the Site Assessment Tool!
Bank Margin width
Bank Margin height above invert or bottom of footer
Length of replacement structure
  (may need additional length to tie into existing banks)
What Material Do I Need?
Same as for grade control features…
Measure largest grade control rock in reference reach
  Use this as a basis for estimating
    Engineer will determine actual size in design

## Slide 55
Estimating Quantities & Costs
Stream Crossing Structure – Backfill / Road Base
Estimating material quantities for ESM practices:
Measure on road shoulder
How big is the road cut?
Figure the area of a trapezoid
  Depth = road elevation – invert of Bottom of Footer Elev.
  Bottom width = structure width +6’ (3’ each side)
  Assume side slopes 1:1
  Calculate top width
  Length = structure length
How much backfill?
Use structure “Area” from vendor’s brochure
Cut “area” – structure “area” = backfill quantity needed

## Slide 56
Estimating Quantities & Costs
Stream Crossing Replacements
Estimating material quantities for ESM practices:
Measure on road shoulder
Use actual installation costs for recent jobs in your region and collect quotes and cost estimates from manufacturers/suppliers.
  Use the RFP for enigineering quotes.

## Slide 57
Estimating Quantities & Costs
Stream Crossing Replacements
Estimating material quantities for ESM practices:
Measure on road shoulder
Remember stream diversion needs.
Ensure actual extent of excavation and backfill are accounted for.
Include required cover for selected structure and taper of fill each direction.
How will the job be broken down?
Who is responsible for what?
What materials and services were quoted?
Make sure that you know the breakdown and don’t overlook the basics

## Slide 58
Estimating Quantities & Costs
Stream Crossing Replacements
Estimating material quantities for ESM practices:
Measure on road shoulder
Be sure to include ancillary structures to the crossing structure, including:
Headwalls
wing walls
bank stabilization structures
… and how it’s going to get done
Labor & equipment

## Slide 59
Estimating Quantities & Costs
Stream Crossing Replacements
Estimating material quantities for ESM practices:
Measure on road shoulder
Don’t forget E&S Requirements!

## Slide 60
  Determine plan and practices. Then determine material needs for each practice. Combine the itemized quantities for a total plan estimate.
  This will help you:
  Determine accuracy of grant applications
  Compare bids and recognize bid miscalculations
  Monitor material usage, overruns, and potential misappropriation of grant funds
  Correlate material amounts with total project costs to estimate contractor costs.
Estimating Quantities & Costs
In conclusion:

## Slide 61
Estimating Quantities & Costs
From beginning to end,
What’s it going to take?

## Slide 62
  Estimating Quantities & Costs
  For DGLVR Projects
Reference sites for estimating material needs:
https://www.dirtandgravel.psu.edu/general-resources/dglvr-materials-calculator
https://www.calculatorsoup.com/calculators/construction/roadway.php