## Slide 1
Sectional Fill
Dirt Gravel and Low Volume Road Program
WEBINAR
3/2/23, 9am
CDGRS
Eric Nevel
ern106@psu.edu
Steve Bloser
smb201@psu.edu
If you are reading this, then you are successfully seeing the webinar video. Webinar audio should be automatic through your computer (or click “join audio”), and options can be accessed in the “audio options” button on the bottom left. If your computer audio is not working, you can listen on your phone by dialing 646-876-9923.

## Slide 2
Purpose:
  Refresher on Road fill and some issues seen on fill projects.
  Overview of “Sectional Fill” as an alternative to “Continuous Fill
Filling Road Cross-Section
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 3
Sectional Fill
  Introduction
  Continuous Fill
  Issues seen with Continuous fill projects
  Sectional Fill Alternative
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 4
Entrenched Roads
A 100-year-old road that loses 1/2 inch of material that is not replaced each year will be entrenched 4’ today.
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 5
Filling Road Cross-Section
Road Base: ESMPs
Entrenched Roads
Lower than surrounding ground on both sides
Make it impossible to get water off the road
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 6
Traditional Maintenance:
Clean ditches and regrade, repeat, repeat, repeat
Road gets lower year by year
Ditches drain directly to stream
Traditional Practices
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 7
Sectional Fill
  Introduction
  Continuous Fill
  Issues seen with Continuous fill projects
  Sectional Fill Alternative
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 8
Road Fill
This is only a quick refresher
Road Fill:
2 Hour Remote Training recorded 5/2021
Recording and PPT Available
  www.dirtandgravelroad.org
  Education/Training – Remote Learning Center
Background – example projects - fill types – RFP – more

## Slide 9
Avoid Concentrating Drainage
Minimize Flow Volumes
Reduce Effects of Concentrated Drainage
Prevent Surface Erosion
Reduce Cost and Frequency of Road Maintenance
ESMP
These are the goals of ALL of the practices in the DGLVR Program
Notes: ALL ESMPs have these five goals
These five principles are the goals of ALL of the Environmentally Sensitive Maintenance Practices we will discuss in the next two days.

## Slide 10
Figures not drawn to scale.
100
102
Continuous Fill
104
106
108
110
Entrenched Road
ditch
flow
ditch
flow

## Slide 11
Figures not drawn to scale.
100
102
ditch
flow
ditch
flow
104
106
108
110
Road
Fill
Entrenched Road
Continuous Fill
Continuous Fill

## Slide 12
Figures not drawn to scale.
100
102
104
106
108
110
Road
Fill
New pipes
Sheet flow
Entrenched Road
Continuous Fill
Continuous Fill
ditch
flow
ditch
flow

## Slide 13
Drainage Disconnection and infiltration are the goals of the DGLVR Program
Road Fill
Hallmarks of the DGLVR program
Keeping sediment & excess runoff out of the stream
Getting water into the ground

## Slide 14
No ditch!
Huntingdon County – Red Rose Road – 6/6
2020
2001
long term improvement!
pipes
Continuous Fill
Notes: DSA Placed Next Year
A year later the DSA was applied to finish the project.

## Slide 15
Road Fill
850’ tall
(300’x160’)
Past
5
years
Of
FILL
Program uses over 300,000 tons annually (13,500+ tri-axles)

## Slide 16
Road Fill
This is only a quick refresher
Road Fill:
2 Hour Remote Training recorded 5/2021
Recording and PPT Available
  www.dirtandgravelroad.org
  Education/Training – Remote Learning Center
Background – example projects - fill types – RFP – more

## Slide 17
Sectional Fill
  Introduction
  Continuous Fill
  Issues seen with Continuous fill projects
  Sectional Fill Alternative
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 18
Road Fill
Dollar for Dollar, one of the best drainage improvement practice available when done correctly.
Some issues seen in the field:
Not achieving sheet flow (not enough fill)
Not building above ground elevation
No surface features = water still runs down road even though it is not entrenched
Filling the Road
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 19
Completed Project: Road fill & underdrain
Road filled ~18”, but did not achieve sheet flow
Filling the Road
Notes: Entrenched – Both Banks Higher – Water Trapped
An entrenched road is where both banks are higher than the road, and water on the road and ditches can’t escape.

## Slide 20
Completed Project: Road fill & turnouts and ditch stabilization
No grade changes in road to divert runoff
Looks good now (months old), what about in 2 years?
Note this is a dead-end road…likely meaning minimal maintenance to keep crown
Filling the Road
Notes: Entrenched – Both Banks Higher – Water Trapped
An entrenched road is where both banks are higher than the road, and water on the road and ditches can’t escape.

## Slide 21
Completed Project (~$100K): Road fill & cross pipes on steep hill
Water is unable to reach ditch or new cross pipes.
Fill higher than lower side of road.
Need grade changes to divert runoff!
Filling the Road
Pipe is dry
Lower ground
Notes: Entrenched – Both Banks Higher – Water Trapped
An entrenched road is where both banks are higher than the road, and water on the road and ditches can’t escape.

## Slide 22
Completed Project: Road fill & turnouts
After 2 years, water running down road again
Lack of maintenance was again an issue
Filling the Road
Notes: Entrenched – Both Banks Higher – Water Trapped
An entrenched road is where both banks are higher than the road, and water on the road and ditches can’t escape.

## Slide 23
Road Fill
Improvement option 1: Overfill the road
Road Fill settles
Traffic and erosion wear surface away
Ensure sheet flow in year 10, not just year 1
Filling the Road
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 24
SUB-SOIL
ROADWAY
TOP-SOIL
Minimum elevation for sheet flow
How: Where banks are higher on both sides of the road
Filling the Road
Notes: Entrenched – Both Banks Higher – Water Trapped
An entrenched road is where both banks are higher than the road, and water on the road and ditches can’t escape.

## Slide 25
SUB-SOIL
ROADWAY
TOP-SOIL
ELIMINATED BANK
REDUCED BANK HEIGHT
FILL
Minimum elevation
Filling the Road
Notes: Fill To Eliminate Downslope Bank and Ditch – Can Sheet Flow ½ Road, and Create More Outlet Options For Pipes – Place To Put Snow
By filling the road high enough to eliminate the downslope bank and ditch, water can sheet flow off the downslope side, and pipes from the upslope ditch can be outletted without a high maintenance tail ditch. In addition, you now have some place to put the snow when you plow.

## Slide 26
SUB-SOIL
ROADWAY
TOP-SOIL
Minor irregularities could still trap water on road surface
How: Where banks are higher on both sides of the road
Filling the Road
NEW ESM Training Updates for 2023
Notes: Entrenched – Both Banks Higher – Water Trapped
An entrenched road is where both banks are higher than the road, and water on the road and ditches can’t escape.

## Slide 27
SUB-SOIL
ROADWAY
TOP-SOIL
But HIGHER is better!
Better draining & longer lasting.
Filling the Road
NEW ESM Training Updates for 2023
Notes: Entrenched – Both Banks Higher – Water Trapped
An entrenched road is where both banks are higher than the road, and water on the road and ditches can’t escape.

## Slide 28
SUB-SOIL
ROADWAY
TOP-SOIL
ELIMINATED BANK
REDUCED BANK HEIGHT
FILL
Higher is better!
Filling the Road
NEW ESM Training Updates for 2023
Notes: Fill To Eliminate Downslope Bank and Ditch – Can Sheet Flow ½ Road, and Create More Outlet Options For Pipes – Place To Put Snow
By filling the road high enough to eliminate the downslope bank and ditch, water can sheet flow off the downslope side, and pipes from the upslope ditch can be outletted without a high maintenance tail ditch. In addition, you now have some place to put the snow when you plow.

## Slide 29
Fill Above Existing Terrain:
  Goal is to promote long-term sheet flow. Consider settling and future erosion.
  Final road elevation should be a foot or more above natural ground for long-term drainage.
  Prevents road from eroding below road berms.
  Over filling is vital to long-term benefits
Filling the Road
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 30
Whenever possible or necessary strive to elevate the road surface by building an embankment
Fill the hole, build a foundation, and elevate the road surface
Scale exaggerated to show concept
Filling the Road
Notes: Fill To Eliminate Downslope Bank and Ditch – Can Sheet Flow ½ Road, and Create More Outlet Options For Pipes – Place To Put Snow
By filling the road high enough to eliminate the downslope bank and ditch, water can sheet flow off the downslope side, and pipes from the upslope ditch can be outletted without a high maintenance tail ditch. In addition, you now have some place to put the snow when you plow.

## Slide 31
surat-thani-thailand-oct-25-260nw-1095967559
http://www.envicom.eu/en/portfolio-posts/sizing-and-calculation-of-a-supporting-structure-necessary-to-ensure-stability-of-an-embankment-road-infrastructure-2/
There is a reason why most major roads are elevated
We can utilize this concept on a smaller scale.
Whenever possible or necessary strive to elevate the road surface above the terrain by building an embankment
Filling the Road
Notes: Fill To Eliminate Downslope Bank and Ditch – Can Sheet Flow ½ Road, and Create More Outlet Options For Pipes – Place To Put Snow
By filling the road high enough to eliminate the downslope bank and ditch, water can sheet flow off the downslope side, and pipes from the upslope ditch can be outletted without a high maintenance tail ditch. In addition, you now have some place to put the snow when you plow.

## Slide 32
Strive to elevate the road surface by building an embankment
Often called “turnpiking”
Filling the Road
Notes: Fill To Eliminate Downslope Bank and Ditch – Can Sheet Flow ½ Road, and Create More Outlet Options For Pipes – Place To Put Snow
By filling the road high enough to eliminate the downslope bank and ditch, water can sheet flow off the downslope side, and pipes from the upslope ditch can be outletted without a high maintenance tail ditch. In addition, you now have some place to put the snow when you plow.

## Slide 33
Strive to elevate the road surface by building an embankment
Often called “turnpiking”
Filling the Road
Notes: Fill To Eliminate Downslope Bank and Ditch – Can Sheet Flow ½ Road, and Create More Outlet Options For Pipes – Place To Put Snow
By filling the road high enough to eliminate the downslope bank and ditch, water can sheet flow off the downslope side, and pipes from the upslope ditch can be outletted without a high maintenance tail ditch. In addition, you now have some place to put the snow when you plow.

## Slide 34
No ditch!
2020
2001
long term improvement!
pipes
Continuous Fill
Why does it work 20 years later?
Road Was Overfilled
Included two grade breaks
Maintenance
Notes: DSA Placed Next Year
A year later the DSA was applied to finish the project.

## Slide 35
Road Fill
Improvement option 2: Sectional Fill
Filling the Road
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 36
Sectional Fill
  Introduction
  Continuous Fill
  Issues seen with Continuous fill projects
  Sectional Fill Alternative
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 37
Sectional Fill:
  When you can’t fill the entire road due to logistics, lack of material and/or cost
  Transition into and out of road fill.
  Short section of fill forces ditch turnout and provides cover for a new cross pipe.
  Can be more effective and less costly than continuous fill
Sectional Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 38
Figures not drawn to scale.
100
102
104
106
108
110
Entrenched Road
Sectional Fill
Ditch
Fl ow
D itch
Flow

## Slide 39
Figures not drawn to scale.
100
102
ditch
flow
ditch
flow
104
106
108
110
Entrenched Road
sectional Fill
Road
Fill
no fill
no fill
Sectional Fill

## Slide 40
Sectional Fill
Figures not drawn to scale.
100
102
104
106
108
110
Fill
Fill
No Fill section,
could be 50’, could be 200’

## Slide 41
Entrenched Road
sectional Fill
On hills, a series of sectional fill sections can be less costly and more effective than filling the full road length
Limitations on steep slopes
Sectional Fill

## Slide 42
McKean Cty – Prospect Rd – 1/7
BEFORE
Sectional Fill

## Slide 43
McKean Cty – Prospect Rd – 1/7
Sectional Fill

## Slide 44
McKean Cty – Prospect Rd – 2/7
BEFORE
Sectional Fill

## Slide 45
Adding Fill
McKean Cty – Prospect Rd – 3/7
Enough fill used to
build crown
reestablish ditch function
reduce the flow volume reaching stream.
Sectional Fill

## Slide 46
At a select location near the project midpoint enough fill is used to create ditch outlets.
McKean Cty – Prospect Rd – 4/7
Sectional Fill

## Slide 47
A crosspipe and turn-out are installed in the elevated road section.
elevated
still entrenched here
AFTER
McKean Cty – Prospect Rd – 5/7
Sectional Fill
Limitations on steep slopes

## Slide 48
Elevated road and ditches relieves ditch flow volumes, reduces erosion and road problems.
AFTER
McKean Cty – Prospect Rd – 6/7
elevated
still entrenched here
Sectional Fill

## Slide 49
Elevated road and ditches relieves ditch flow volumes, reduces erosion and road problems.
AFTER
McKean Cty – Prospect Rd – 7/7
elevated
still entrenched here
Sectional Fill

## Slide 50
No fill
No fill
Susquehanna County
Road Fill Overview
Fill or “extended grade break”

## Slide 51
No fill
No fill
Susquehanna County
Road Fill Overview
Fill or “extended grade break”

## Slide 52
Sectional Fill Advantages:
  Less Costly than continuous fill (uses less fill)
  Still provides benefits of fill (improves road, allows turnouts and pipes, etc)
  More “neglect –proof”: Excellent option in locations where you know maintenance will be limited.
Sectional Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 53
Sectional Fill Advantages:
  Less Costly than continuous fill (uses less fill)
  Still provides benefits of fill (improves road, allows turnouts and pipes, etc)
  More “neglect –proof”: Excellent option in locations where you know maintenance will be limited.
  Continuous Fill Reminders:
  Overfill the road (for long term sheet flow)
  Use surface drainage features when possible.
Sectional Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 54
Questions? Discussion?
Sectional Fill Advantages:
  Less Costly than continuous fill (uses less fill)
  Still provides benefits of fill (improves road, allows turnouts and pipes, etc)
  More “neglect –proof”: Excellent option in locations where you know maintenance will be limited.
  Continuous Fill Reminders:
  Overfill the road (for long term sheet flow)
  Use surface drainage features when possible.
Road Fill:
2 Hour Remote Training recorded 5/2021
Recording and PPT Available
  www.dirtandgravelroad.org
  Education/Training – Remote Learning Center
Background – example projects - fill types – RFP – more
Notes: This Section – Bank Management
In this section we will focus on the management of road banks.