## Slide 1
Shallow Crosspipes
Dirt Gravel and Low Volume Road Program
WEBINAR
3/23/23, 9am
CDGRS
Dave Creamer
dmc159@psu.edu
Steve Bloser
smb201@psu.edu
If you are reading this, then you are successfully seeing the webinar video. Webinar audio should be automatic through your computer (or click “join audio”), and options can be accessed in the “audio options” button on the bottom left. If your computer audio is not working, you can listen on your phone by dialing 646-876-9923.

## Slide 2
Why Shallow Crosspipes?
  Probably one of the most common recommendations on QAQCs:
    More and better crosspipes (angle, hw/ew)
    Pipes are too deep
    Utilize shallow crosspipes
    Use grade breaks if possible
Filling Road Cross-Section
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 3
Ex 1/5
Pipe inlet too deep!
Ditch Outlets: Traditional Practices
Pipes to Deep

## Slide 4
Ex 2/5
Pipe inlet too deep!
Ditch Outlets: Traditional Practices
Pipes to Deep

## Slide 5
Shallow Pipe Installation: Installing a crosspipe to outlet at natural ground elevation. This typically involves a shallower trench and additional fill when compared to a traditional installation.
Let’s compare…
SHALLOW Crosspipes
Ditch Outlets: ESMPs

## Slide 6
Traditional “Deep” Installation
SHALLOW Crosspipes
Ditch Outlets: ESMPs
Road
31”
>12”
31”
Compacted
Pipe
Fill
19”
15” inside diameter
Outlet Trench
Required!
Natural Ground Elevation

## Slide 7
Traditional “Deep” Installation
Natural Ground Elevation
Outlet Trench
Required!
SHALLOW Crosspipes
Ditch Outlets: ESMPs

## Slide 8
Shallow Pipe Installation
Excavate trench
SHALLOW Crosspipes
Ditch Outlets: ESMPs

## Slide 9
Shallow Pipe Installation
Compacted
Pipe
Fill
31”
>12”
Pipe bottom is at natural ground elevation: No outlet trench!
19”
15” inside diameter
SHALLOW Crosspipes
Ditch Outlets: ESMPs

## Slide 10
>12”
Compacted
Pipe
Fill
31”
>12”
Compacted
Pipe Fill
Road
Roadbed
old road
Roadbed
Traditional
Cover obtained by digging
Cover obtained by filling
Shallow
15” inside diameter
15” inside diameter
new road
Pipe bottom is at natural ground elevation: No outlet trench!
Outlet Trench
Required!
SHALLOW Crosspipes
Ditch Outlets: ESMPs

## Slide 11
Why Shallow Pipes?
Outlet water to natural ground instead of into a hole!
Reduce maintenance
Encourage infiltration and recharge
Reduce problems associated with deep pipes
SHALLOW Crosspipes
Ditch Outlets: ESMPs

## Slide 12
The Bottom Line:
Don’t use road surface elevation to determine pipe elevation!
Use ground elevation at outlet to determine pipe elevation!
SHALLOW Crosspipes
Ditch Outlets: ESMPs

## Slide 13
Why Shallow Crosspipes?
This program is all about outlets!
Filling Road Cross-Section
Road Fill
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 14
Shallow Crosspipes
  Some History
  Getting more of them
  What do you need in your applications
  Tips for a good Installation.
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 15
Slide from the 2002 Workshop Orientation

## Slide 16
SHALLOW Crosspipe Installation
ENVIRONMENTALLY SENSITIVE
MAINTENANCE PRACTICES

## Slide 17
Shallow Crosspipes
  Some History
  Getting more of them
  What do you need in your applications
  Tips for a good Installation.
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 18
Shallow Crosspipes
  Give new outlets a lot of points in your ranking.
    (Like A lot!)
    Talk to landowners yourself.
    (It will be insightful and rewarding.)
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 19
Project from 2015
DGR Project in Mercer County: $100K Spent, $6K in kind
AFTER
Notes: good

## Slide 20
Pipe outlet too deep!
Ex 3/5
Pipes too Deep
TRADITIONAL ROAD
MAINTENANCE PRACTICES

## Slide 21
Shallow Crosspipes
  Some History
  Getting more of them
  What do you need in your applications
  Tips for a good Installation.
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 22
Shallow Crosspipes
The Shallow Pipe Requires Cover!
(Think Road Fill)
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 23
Pipe outletted at natural ground elevation
Material imported to provide cover
Filling the Road
Notes: Fill To Eliminate Downslope Bank and Ditch – Can Sheet Flow ½ Road, and Create More Outlet Options For Pipes – Place To Put Snow
By filling the road high enough to eliminate the downslope bank and ditch, water can sheet flow off the downslope side, and pipes from the upslope ditch can be outletted without a high maintenance tail ditch. In addition, you now have some place to put the snow when you plow.

## Slide 24
Sectional Fill
Figures not drawn to scale.
100
102
104
106
108
110
Fill
Fill
No Fill section,
could be 50’, could be 200’

## Slide 25
Entrenched Road
sectional Fill
On hills, a series of sectional fill sections can be less costly and more effective than filling the full road length
Limitations on steep slopes
Sectional Fill

## Slide 26
A crosspipe and turn-out are installed in the elevated road section.
elevated
still entrenched here
AFTER
Sectional Fill
Limitations on steep slopes

## Slide 27
Elevated road and ditches relieves ditch flow volumes, reduces erosion and road problems.
AFTER
elevated
still entrenched here
Sectional Fill

## Slide 28
Shallow Crosspipes
The Shallow Pipe Requires Pipe!
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 29
12, 15, 18 inch ???
Should always be longer than a traditional pipe.
ENVIRONMENTALLY SENSITIVE
MAINTENANCE PRACTICES

## Slide 30
Shallow Crosspipes
  All Pipes Require Head and End Walls!
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 31
Inlet Protection

## Slide 32
Proper Crosspipe Installation
Inlet and Outlet Protection
Ditch Outlets ESMPs

## Slide 33
Shallow Crosspipes
  Some History
  Getting more of them
  What do you need in your applications
  Tips for a good Installation.
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 34
Undersized Pipes
road surface
NO
bank erosion
bank erosion
ditch flow
ditch flow
Proper Pipe Alignment
YES
Install pipes in direction of flow
ENVIRONMENTALLY SENSITIVE
MAINTENANCE PRACTICES

## Slide 35
road surface
ditch flow
ditch flow
Don’t forget headwalls!
Proper Pipe Alignment
ENVIRONMENTALLY SENSITIVE
MAINTENANCE PRACTICES

## Slide 36
Placement:
Inlet should be located in existing ditch line.
Potter
Proper Crosspipe Installation
Place Pipe in Trench
Ditch Outlets ESMPs

## Slide 37: Arkansas Nature Conservancy
“Workshop-like” event sponsored by the Nature Conservancy in Arkansas

## Slide 38
Shallow Crosspipes
  New Outlets and Road Fill Projects are all ways good Investments.
  New outlets need Landowner agreements.
  Longer pipes and extra pipe bedding/cover need to included in your grant apps.
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.

## Slide 39
Shallow Crosspipes
  Questions?
Notes: Helps With Drainage On Entrenched Roads
This technique can really help with drainage issues on entrenched roads.