## Slide 1
CDGRS
Tim Ziegler
tmz115@psu.edu
Thanks to Sullivan and Cameron County for example projects
Small Slip and Slide Repair
Dirt Gravel and Low Volume Road Program
January 26, 2023
9am
If you are reading this, then you are successfully seeing the webinar video. Webinar audio should be automatic through your computer (or click “join audio”), and options can be accessed in the “audio options” button on the bottom left. If your computer audio is not working, you can listen on your phone by dialing 312-626-6799.

## Slide 2
Small Slip and Slide Repair
The Basics
A Plan of Attack
Example 1: Sizer Run Rd & Hunts Run Rd, Cameron County
Example 2: Lick Creek Rd, Schrader Creek Rd, South Black Creek Rd Sullivan County
Credit: Cameron County CD

## Slide 3
Diagnosing types and causes of roadside slope instability
and simple, cost-effective techniques for road bank repair
Small Slide and Slip Repair
Credit: Pike County CD

## Slide 4
Don’t let your most valuable assets slip away from you!
Small Slide and Slip Repair

## Slide 5
A User Guide to Diagnosing and Repairing Failing Road Banks
This guide describes common slope failures, the conditions that contribute to the failures and stabilization techniques that can be used to repair damaged slopes.
The guide reviews common causes of slope failure and methods of stabilizing slopes based on local site conditions, such as type of slope failure, type of soil, and drainage.
Scenarios for eight common slope failures are presented based on combinations of the site conditions.
As you will see, the recommended remedy for most all small slope failures is the same or similar in all the scenarios.
https://dot.state.mn.us/research/reports/2017/201717G.pdf
Small Slide and Slip Repair

## Slide 6
A User Guide to Diagnosing and Repairing Failing Road Banks
Slopes can be stabilized by adding a surface cover to the slope, excavating, and changing (or regrading) the slope geometry, adding support structures to reinforce the slope, or using drainage to control the groundwater in slope material.
Three site conditions should be considered when choosing an appropriate method for stabilizing a slope:
 Type of slope failure
 Type of soil
 Presence of groundwater (poor drainage)
Small Slide and Slip Repair

## Slide 7
Type of Slope Failure:
Slope failure is generally classified as either a rotational slide or a surficial soil creep.
Rotational slide failures
  circular pattern
  leave behind exposed soil
Creep failures
  slow‐moving
  material gradually moves downhill
  Surface cracking can indicate the slope is nearing a rotational slide failure.
  Common causes of creep failure are seasonal freeze‐thaw cycles and inadequate shear strength properties in soil. Bent trees or signs can indicate creep failure.
Small Slide and Slip Repair

## Slide 8
Type of Slope Failure:
(Rotational Slide)
Small Slide and Slip Repair

## Slide 9
Type of Soil:
Two soil types to consider:
Cohesive soils (such as silt and clay)
Granular soils (sand)
Soil types can often be distinguished by a visual inspection, but sometimes laboratory testing is required.
Slopes made of granular or sandy soil are less likely to experience deep rotational slides.
Slopes made of cohesive soils like clay and silt usually have more drainage concerns and are more susceptible to seasonal frost heave.
Small Slide and Slip Repair

## Slide 10
Presence of Groundwater (poor drainage):
The third major site condition that affects a slope is poor drainage. Drainage is considered poor if groundwater lowers soil shear strength and leads to failure.
Groundwater has a significant effect on shear strength. In the research study, removing groundwater provided the greatest difference in the output factor of safety.
Small Slide and Slip Repair

## Slide 11
Diagnosing the Cure:
Determining the site conditions that most closely match the type of slope failure, type of soil, and presence of groundwater will guide you to one of eight practical repair methods to use.
Small Slide and Slip Repair

## Slide 12
Diagnosing the Cure:
To determine the appropriate scenario:
First, determine the failure type (rotational or creep).
Next, choose the soil type of the slope material (cohesive or granular).
Then determine whether groundwater is present at the site.
  *Note: “Poor drainage” is interchangeable with “groundwater concerns.”
Small Slide and Slip Repair
Credit: Pike County CD

## Slide 13
Small Slip and Slide Repair
The Basics
A Plan of Attack
Example 1: Sizer Run Rd & Hunts Run Rd, Cameron County
Example 2: Lick Creek Rd, Schrader Creek Rd, South Black Creek Rd Sullivan County
Credit: Cameron County CD

## Slide 14
Plan of Attack:
Scenarios 1 through 4-
Site Conditions:
Rotational failure
Cohesive or sandy soil
With or without groundwater concerns
Recommended Stabilization Approach for all small rotational failures:
Remove and replace poor soils
Add drainage features
Add vegetative cover, hard armoring or both (hard armor sandy soils to prevent erosion)
Small Slide and Slip Repair

## Slide 15
Plan of Attack:
Drainage features remove groundwater
Fill‐and‐regrade work adds stability
Place drains near the toe of the slope
If significant rotational failure has already occurred, rebuild the slope with as low of a slope angle as possible.
Small Slide and Slip Repair

## Slide 16
Plan of Attack:
Specific to Sandy Soils:
Surface cover is very important for slopes with granular soil because erosion is a concern. Surface erosion can cause geometric inconsistencies that lead to failure. Erosion can often cause washout failure. Use a hard armor surface cover (riprap or coarse gravel).
Small Slide and Slip Repair
Credit: Wayne County CD

## Slide 17
Plan of Attack:
Scenarios 5 through 8-
Site Conditions:
Creep failure
Cohesive or sandy soil
With or without groundwater concerns
Recommended Stabilization Approach for all small creep failures:
Remove and replace poor soils
Add drainage features
Add vegetative cover, hard armoring or both (hard armor sandy soils to prevent erosion)
Small Slide and Slip Repair
Credit: Wayne County CD

## Slide 18
Plan of Attack:
Drainage features remove groundwater
Fill‐and‐regrade work adds stability
Place drains near the toe of the slope
For creep failures, if soil cannot be removed and replaced, use a buttress at toe of the slope to stabilize the bank.
Small Slide and Slip Repair

## Slide 19
Plan of Attack:
Repair for Rotational Failures (Slumps)
With blocks, geosynthetics, competent fill, drainage, and cover (to control erosion)
Must excavate below slip plane
Small Slide and Slip Repair

## Slide 20
Plan of Attack:
Repair for Rotational Failures (Slumps)
With Riprap, geosynthetics, drainage
Must excavate below slip plane
Small Slide and Slip Repair

## Slide 21
Plan of Attack:
Repair for Creep Failures (Ooze)
With block, riprap, geosynthetics, drainage
Must excavate below slip plane
Buttress
Small Slide and Slip Repair

## Slide 22
Plan of Attack:
Repair concerns for all slope failures:
Bank instability caused by over-steepening can often be corrected by “laying the bank back” (shaping to a lesser grade). Most common on upslope road banks.
Loss of a stable toe from aggressive ditch cleaning, streambank erosion, etc. can trigger slope failure.
Adding drainage features to your stabilization plan is cheap insurance against unforeseen problems.
Don’t underestimate the value of vegetation (or lack of) in maintaining bank stability, especially woody vegetation.
Don’t forget the benefits of fill to address bank instability…..
Small Slide and Slip Repair

## Slide 23
Fall Brook Road Fill Slope Stabilization Project
Credit: Wayne County CD
Small Slide and Slip Repair

## Slide 24
Fall Brook Road Fill Slope Stabilization Project
Credit: Wayne County CD
Small Slide and Slip Repair

## Slide 25
Fall Brook Road Fill Slope Stabilization Project
Knee replacement, hip replacement, toe replacement…
Credit: Wayne County CD
Small Slide and Slip Repair

## Slide 26
Small Slip and Slide Repair
The Basics
A Plan of Attack
Example 1: Sizer Run Rd & Hunts Run Rd, Cameron County
Example 2: Lick Creek Rd, Schrader Creek Rd, South Black Creek Rd Sullivan County

## Slide 27: Geosynthetic Reinforced Soil (GRS) Slide Repair
Credit: Cameron County CD

## Slide 28
Credit: Cameron County CD
Geosynthetic can be wrapped or pinched between facing block/rock

## Slide 29: Benefits of GRS
Cost $$$
  Traditional fixes are pricey
    Significant resources
    Specialized equipment
  Done with readily available materials
Can typically be done with township labor
Can be completed in few days
GRS repairs are not applicable to all sites
Credit: Cameron County CD

## Slide 30: Sizer Run – Shippen Township
200’ long 8’ high
Used Contractor for implementation
90 concrete blocks
2 new pipes
24 loads of 2RC
4 Days to complete
$23,200.00
Credit: Cameron County CD

## Slide 31
Credit: Cameron County CD
Sizer Run
GRS stabilization method used block wall extends to slip plane

## Slide 32: Hunts Run Road – Lumber Township
2 different slides along road
Hunts Run Class A Wild Trout
Completed with Township Labor
Both approximately 140’ x 6’
100 mafia block
30 loads of 2RC
Approximately $29,000.00
Credit: Cameron County CD

## Slide 33
Credit: Cameron County CD
Hunts Run Road
Stabilized both upslope
and downslope banks

## Slide 34
Credit: Cameron County CD
Hunts Run Road
Lower bank repair used GRS method with block wall

## Slide 35
Small Slip and Slide Repair
The Basics
A Plan of Attack
Example 1: Sizer Run Rd & Hunts Run Rd, Cameron County
Example 2: Lick Creek Rd, Schrader Creek Rd, South Black Creek Rd Sullivan County
Credit: Cameron County CD

## Slide 36: AVOID THIS….
AND MAKE A PLAN
Credit: Sullivan County CD

## Slide 37: Lick Creek Road Sullivan County, PA
Credit: Sullivan County CD

## Slide 38: Lick Creek Road Bank Stabilization Plan
Credit:
Sullivan County CD

## Slide 39: Lick Creek Road Before Stacked Concrete Wall
Bank sloughing onto roadway
Excavating for drain and rock overlay
Credit: Sullivan County CD

## Slide 40: Stacked Concrete Wall #1 Completed
Lick Creek Road
Credit: Sullivan County CD

## Slide 41
Stacked Concrete Wall #2 Completed
Lick Creek Road
Rock overlay replaces poor soils
Footer drain and pipe remove water
Credit: Sullivan County CD

## Slide 42: Schrader Creek Road Sullivan County, PA
Credit: Sullivan County CD

## Slide 43: Schrader Creek Road Before Stacked Rock Wall
Road Bank / Stream Bank Failing
Slip Encroaching on Road
Credit: Sullivan County CD

## Slide 44: Schrader Creek Road Coompleted Stacked Rock Wall
Large Rock embedded into channel make stable toe
Road shifted for stable bank angle without stream encroachment
Credit: Sullivan County CD

## Slide 45: South Black Creek Road Sullivan County, PA
Credit: Sullivan County CD

## Slide 46: South Black Creek Road Bank Failure Due To Surface Erosion Before Outfall Pipe Stabilization
Credit: Sullivan County CD

## Slide 47: South Black Creek Road Outfall Pipe Stabilization
Reconstructed bank at pipe outfall
Rock at stable angle with large rock at toe
Credit: Sullivan County CD

## Slide 48
Questions?
Or let us know your experiences.
CDGRS
Tim Ziegler
tmz115@psu.edu
Thanks to Sullivan and Cameron County for example projects