## Slide 1
CDGRS
Steve Bloser
smb201@psu.edu
SCC
Roy Richardson
rrichardso@pa.gov
SCC
Sherri Law
shlaw@pa.gov
Stream Notification and Exemptions
Dirt Gravel and Low Volume Road Program
WEBINAR
1/5/22
Starts 9am
If you are reading this, then you are successfully seeing the webinar video. Webinar audio should be automatic through your computer (or click “join audio”), and options can be accessed in the “audio options” button on the bottom left. If your computer audio is not working, you can listen on your phone by dialing 312-626-6799.

## Slide 2
Notifications:
Reminder and review of process
Added input for exemptions
Exemptions:
Review process
A few examples
Stream Notification and Exemptions

## Slide 3
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Where the DGLVR Stream Crossing Policy Applies
  where streams, including intermittent channels, with identified bed and banks are flowing into the road or the uphill ditch.
  All stream crossing replacements funded in whole or in part with DGLVR funds, or listed as in-kind on a DGLVR Project, must follow the DGLVR Stream Crossing Design & Installation Standard
    unless an “Exemption from DGLVR Stream Crossing Standard” is applicable

## Slide 4
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Where the
DGLVR Stream
Crossing Policy
Applies
Example 1
Looking upslope from road

## Slide 5
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Where the
DGLVR Stream
Crossing Policy
Applies
Example 1
Looking upslope from road

## Slide 6
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Where the
DGLVR Stream
Crossing Policy
Applies
Example 2
Looking upslope from road

## Slide 7
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Where the
DGLVR Stream
Crossing Policy
Applies
Example 3
Looking upslope from road

## Slide 8
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Where the
DGLVR Stream
Crossing Policy
Applies
Example 4
Looking upslope from road

## Slide 9
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Stream Crossing Notifications
  With the new standard in place, are stream crossing replacement notifications still required?

## Slide 10
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Stream Crossing Notifications
  With the new standard in place, are stream crossing replacement notifications still required?
  Yes: (DGLVR Administrative Manual 7.1.2.2)
  SCC Notification: Conservation districts are required to notify the State Conservation Commission (SCC) of proposed stream crossing replacements as soon as practical before a contract is signed. An online notification system is available by logging in to the Center for Dirt and Gravel Road Studies website (same log-in as accessing the GIS system) at www.dirtandgravelroads.org.

## Slide 11
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Stream Crossing Notifications
  Why are notifications still required?

## Slide 12
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Stream Crossing Notifications
  Why are notifications still required?
  To get ahead of potential issues
  To gauge upcoming workload
  To ensure adequate TA is available

## Slide 13
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Stream Crossing Notifications
  Are notifications required for exempt crossings?

## Slide 14
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Stream Crossing Notifications
  Are notifications required for exempt crossings?
  Yes: (DGLVR Administrative Manual 7.1.3)
  Complete the “Automatic Exemption from the DGLVR Stream Crossing Standard” form (Appendix I) and keep it in the project file. Automatic exemptions still need to be reported in the SCC notification system.
  New input selections for exempt crossings in notification system – will review

## Slide 15
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Stream Crossing Notifications
  Where:

## Slide 16
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Basic Information: who, what, where, when

## Slide 17
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Existing Conditions: bankfull and existing structure

## Slide 18
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Project Status

## Slide 19
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Proposed New Structure: if known, what will likely be installed

## Slide 20
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Optional Details: other information and pictures

## Slide 21
Stream Notifications and Exemptions
www.dirtandgravelroads.org
NEW SECTION: Exemptions: must upload either automatic or SCC approve exemption form
Automatic
SCC Approved

## Slide 22
Notifications:
Reminder and review of process
Added input for exemptions
Exemptions:
Review process
A few examples
Stream Notification and Exemptions

## Slide 23
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Two types of exemptions
  Automatic Exemption
    for small channels
    CD may grant without SCC approval
  SCC Approved
    For any circumstance not covered by automatic exemption
  Reminder: All Exemptions
  are only exempt from following DGLVR standard, not any permit or other requirements
  Are still required to be 1.25 BF and ensure stability above and below new structure

## Slide 24
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Automatic Exemptions
  Two scenarios where CD may exempt a crossing:
    < 4’ Bankfull and < 20-acre watershed
    < 4’ Bankfull and < 500’ of “bed and banks” channel
  Must fill out “automatic exemption” form and keep in file.
  Must complete SCC “stream crossing notification” online, including uploading automatic exemption form.
  No SCC approval required.
  Reminder: All Exemptions
  are only exempt from following DGLVR standard, not any permit or other requirements
  Are still required to be 1.25 BF and ensure stability above and below new structure

## Slide 25
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Automatic Exemptions
  Two scenarios where CD may exempt a crossing:
    < 4’ Bankfull and < 20-acre watershed
      Easier, can be done “remotely”
      DGLVR GIS is a good tool, especially with wetness index
    < 4’ Bankfull and < 500’ of “bed and banks” channel
      More difficult, requires field determination
  Reminder: All Exemptions
  are only exempt from following DGLVR standard, not any permit or other requirements
  Are still required to be 1.25 BF and ensure stability above and below new structure

## Slide 26
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Automatic Exemption
Form
  1-page
  Keep in project file
  Upload to notification
  Reminder: All Exemptions
  are only exempt from following DGLVR standard, not any permit or other requirements
  Are still required to be 1.25 BF and ensure stability above and below new structure
Site
Info
Justification

## Slide 27
Stream Notifications and Exemptions
www.dirtandgravelroads.org
BONUS:
Stream stats now available directly in DGLVR GIS
to get watershed areas
DEMO

## Slide 28
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1

## Slide 29
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Site 1 picture
Crossing 1: 36” pipe inlet

## Slide 30
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Site 1 picture
Crossing 1: 9’ Bankfull

## Slide 31
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
2
3
1
Crossing 1:
No USGS blueline
9’ Bankfull
Has streamstats blueline

## Slide 32
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Crossing 1:
No USGS blueline
9’ Bankfull
Has streamstats blueline
Streamstats returns 110 Acre Watershed
Not eligible for automatic waiver
  Bankfull over 4’
  Watershed over 20 acres

## Slide 33
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Site 2 picture
Crossing 2: 24” pipe inlet

## Slide 34
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Site 2 picture
Crossing 2: 5’ bankfull

## Slide 35
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Crossing 2:
No USGS blueline
5’ Bankfull
Has streamstats blueline
Streamstats returns 23 acre watershed

## Slide 36
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Crossing 2:
No USGS blueline
5’ Bankfull
Has streamstats blueline
Streamstats returns 23 acre watershed
Manual Double check = 23 acre watershed

## Slide 37
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Crossing 2:
No USGS blueline
5’ Bankfull
Has streamstats blueline
Streamstats returns 23 acre watershed
Manual Double check = 23 acre watershed
Not Eligible: bankfull >4’

## Slide 38
Stream Notifications and Exemptions
www.dirtandgravelroads.org
3
1
Crossing 2:
No USGS blueline
3’ Bankfull
Has streamstats blueline
Streamstats returns 23 acre watershed
Manual Double check = 23 acre watershed
Let’s pretend bankfull is 3’.
Is it eligible?
2

## Slide 39
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Crossing 2:
No USGS blueline
3’ Bankfull
Has streamstats blueline
Streamstats returns 23 acre watershed
Manual Double check = 23 acre watershed
Not automatically eligible based on watershed. Need to see if bed and banks channels ends within 500’ upslope of road
? 500’ ?
Let’s pretend bankfull is 3’.
Is it eligible?

## Slide 40
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Site 3 picture
Crossing 3: 24” inlet

## Slide 41
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Site 3 picture
Crossing 3: 3.5’ bankfull

## Slide 42
Stream Notifications and Exemptions
www.dirtandgravelroads.org
2
3
1
Crossing 3:
No USGS blueline
No streamstats blueline
3.5’ BF
Manual measurement = 17.3 acre watershed
Eligible for Automatic Waiver

## Slide 43
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Where the
DGLVR Stream
Crossing Policy
Applies
Example 4
Looking upslope from road

## Slide 44
Stream Notifications and Exemptions
www.dirtandgravelroads.org
What if…what if…what if…
  There will always be odd circumstances
  Let not make policy for every possible situation
  For odd circumstance, call the SCC!
Pond or wetland upstream, how do I measure channel length?
My watershed starts as
turnpike drainage?
Channel comes off, hill, to grass swale, to drop inlet.

## Slide 45
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Automatic Exemptions: Example 2
Example 2
Numers Hollow Rd, Henderson Twp, Huntingdon Co

## Slide 46
Stream Notifications and Exemptions
www.dirtandgravelroads.org
SCC Approved Exemptions
  On any other crossing not meeting criterial for automatic exemptions.
  Could be for any variety of reasons, for example:
    Impossible to achieve continuity due to extreme drop or other manmade limitations.
    Channel is urban area is actually a large stormwater channel.
    Other?????
  SCC Exemption form must be submitted to SCC
  Reminder: All Exemptions
  are only exempt from following DGLVR standard, not any permit or other requirements
  Are still required to be 1.25 BF and ensure stability above and below new structure

## Slide 47
Stream Notifications and Exemptions
www.dirtandgravelroads.org
SCC Approval Exemption
Form
  1-page
  Keep in project file
  Upload to notification
  Reminder: All Exemptions
  are only exempt from following DGLVR standard, not any permit or other requirements
  Are still required to be 1.25 BF and ensure stability above and below new structure
Site
Info
Justification

## Slide 48
Stream Notifications and Exemptions
www.dirtandgravelroads.org
SCC Approval
Exemption
Form
  Keep in project file
  Upload to notification
  Reminder: All Exemptions
  are only exempt from following DGLVR standard, not any permit or other requirements
  Are still required to be 1.25 BF and ensure stability above and below new structure
Site
Info
Justification
SCC Use: Approval
SCC Use: additional conditions

## Slide 49
Stream Notifications and Exemptions
www.dirtandgravelroads.org
SCC Approved Exemptions: Example 1
12’ vertical offset
Railroad bridge upstream preventing stream modification
Meets larger stream downstream preventing stream modification
12’ drop in 15’

## Slide 50
Stream Notifications and Exemptions
www.dirtandgravelroads.org
SCC Approved Exemptions: Example 1

## Slide 51
Stream Notifications and Exemptions
www.dirtandgravelroads.org
12’ drop in 15’
Railroad bridge
upstream
SCC Approved Exemptions: Example 1

## Slide 52
Stream Notifications and Exemptions
www.dirtandgravelroads.org
SCC Approved Exemptions: Example 2
Example 2

## Slide 53
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Reminder of Exemption Requirements
  New structures must still be a single span at a minimum of 1.25 times or 125% of the bankfull channel width unless otherwise approved by the SCC.
  Ensure the stability of the channel upstream and downstream. Grade controls must be shown on plan drawings if drawings are required.
    Upstream: Grade control(s) are required immediately (between one and two bankfull widths) upstream of the inlet of the new structure to prevent headcutting (headward erosion lowering channel elevation that moves upstream over time). These grade controls are typically installed at the existing streambed elevation. If a larger structure is installed in a channel with road height limitations, installing a larger structure below the existing streambed elevation without grade control(s) will likely cause a headcut.
    Downstream: Outlet stabilization is required in the form of grade controls, bank armoring, and/or filling in scour holes. Any grade controls are typically installed at the existing streambed elevation. Pipes may need to be extended further off the road, and the erosion potential caused by any elevation drops must be considered.
  Reminder: All Exemptions
  are only exempt from following DGLVR standard, not any permit or other requirements
  Are still required to be 1.25 BF and ensure stability above and below new structure

## Slide 54
Stream Notifications and Exemptions
www.dirtandgravelroads.org
Reminder of Exemption Requirements
  New structures must still be a single span at a minimum of 1.25 times or 125% of the bankfull channel width unless otherwise approved by the SCC.
  Ensure the stability of the channel upstream and downstream. Grade controls must be shown on plan drawings if drawings are required.
    Upstream: Grade control(s) are required immediately (between one and two bankfull widths) upstream of the inlet of the new structure to prevent headcutting (headward erosion lowering channel elevation that moves upstream over time). These grade controls are typically installed at the existing streambed elevation. If a larger structure is installed in a channel with road height limitations, installing a larger structure below the existing streambed elevation without grade control(s) will likely cause a headcut.
    Downstream: Outlet stabilization is required in the form of grade controls, bank armoring, and/or filling in scour holes. Any grade controls are typically installed at the existing streambed elevation. Pipes may need to be extended further off the road, and the erosion potential caused by any elevation drops must be considered.
  Reminder: All Exemptions
  are only exempt from following DGLVR standard, not any permit or other requirements
  Are still required to be 1.25 BF and ensure stability above and below new structure
WHY?
Still want to accommodate larger flows.
Putting a larger structure in without addressing stability could actually make the situation WORSE
Potential headcut upstream by lowering inlet elevation.
Potential increase erosion / road stability issue downstream.