## Slide 1
Underdrain, Storm Sewer
& Infiltration
Notes: Show Quickly

## Slide 2
Introduction
Underdrain
  Carries: groundwater
  Requires: slope/fall to carry water
  Outlets: on the surface
Storm sewer
  Carries: surface water underground
  Requires: slope/fall to carry water
  Outlets: on the surface
Infiltration practices
  Carries: surface water underground
  Requires: flat bottom and correct site conditions to achieve infiltration
  Outlets: underground via infiltration
    With a surface overflow
Notes: Project C

## Slide 3
Underdrain, Storm Sewer
& Infiltration
LVR Overview
Underdrains
Storm Sewer
Infiltration – Structural BMPs

## Slide 4
Underdrains
Notes: Consider Underdrains When:
Wet Ditches, Banks, Spots in Road
Dry Bank and Remove Lubrication
Consider an Underdrain when you see perpetually wet ditches and banks along the road. They can even be installed under the cartway to dry out problem wet spots. When you dry out wet ditches and drain wet banks, you remove lubrication from the equation and make your banks more stable.

## Slide 5
When TO USE:
Groundwater!!!!!
  Saturated road bases
  Perpetually wet ditches and banks
Underdrains
WHERE ROADS ARE CONSISTENTLY
WET FROM GROUNDWATER WATER.
Notes: Consider Underdrains When:
Wet Ditches, Banks, Spots in Road
Dry Bank and Remove Lubrication
Consider an Underdrain when you see perpetually wet ditches and banks along the road. They can even be installed under the cartway to dry out problem wet spots. When you dry out wet ditches and drain wet banks, you remove lubrication from the equation and make your banks more stable.

## Slide 6
Use where ground water issues are affecting the road.
Underdrains

## Slide 7
Underdrains
Example Project #1: Exposed Underdrain
Notes: Discussed in “Banks”
We talked about these buried drains in the “Banks” section.

## Slide 8
1. Excavate Trench
2. Place Geo-textile
3. Add pipe and clean fill
4. Add clean fill
5. Wrap and overlap geo-textile
6. Cover geo-textile
FHWA Geosynthetic Design and Construction Guidelines (Berg, et. al., 1998)
Underdrains
Constructed Stone Underdrain
Notes: Constructed Underdrain:
Built Any Size – For Any Flow
Clean Filter Stone Also Carries Water
Slide of Steps of Construction
A constructed underdrain can be built to any size, to handle any anticipated flow. The clean stone surrounding the drain pipe will carry water as well. I’ve seen a lot of field drains made only of stone. This slide shows the steps of constructing an underdrain.

## Slide 9
Underdrains
Before
Groundwater from pipeline

## Slide 10
Underdrains
During
Underdrain excavation
Ensure trench has positive drainage. Use Laser Level!

## Slide 11
Underdrains
During
Non-Woven Fabric & Perforated Pipe Placement
Non-Woven Fabric
- separates
filters

## Slide 12
Underdrains
During
AASHTO #1 Stone Backfill

## Slide 13
Underdrains
During
AASHTO #1 Stone Backfill

## Slide 14
Underdrains
After

## Slide 15
Underdrains
Pipe outlet
Separate underdrain outlet

## Slide 16
Underdrains
Close up of separate underdrain outlet
Looking from road

## Slide 17
Underdrains
Close up of separate underdrain outlet
Facing road

## Slide 18
Underdrains
Solid Pipe at Outfall.
Solid pipe prevents crushing
Critter guards
Notes: Dig to Desired Width and Depth to Allow For Min. 12” Cover
Ensure Minimum 1% Slope
Line With Geo-Fab
Clean Stone Bedding
Lay Pipe
The trench was excavated to the desired width, and deep enough to allow for sufficient cover of the completed underdrain. The backhoe operator made sure their was at least 1% slope, so the drain would drain . The trench was then lined with enough geo-fabric to overlap on top. Clean stone was laid in the bottom as pipe bedding, and the perforated drain pipe was laid on top of the stone.

## Slide 19
Perforated Pipe
Clean Stone
Example Project #2: Buried Underdrain
During
Wet ditch from seep

## Slide 20
Topsoil w/ Seeding & Mulching.
Maintain ditch shape/profile.
During

## Slide 21
After

## Slide 22
Considerations:
Use clean stone (with no fines) – AASHTO 1 a good choice
Small stone (such as 2A) that is exposed at surface is prone to washouts and clogging.
Cover with min 1’ material – avoid reusing ditch spoils
Use caution installing on slopes – often not needed here
Use constructed stone underdrains wrapped in non-woven geofabric (use of fabric may be local decision)
Outlet separately from ditch drainage when possible
Easy to add underdrain with little effort in fill jobs
Underdrains
Road Base: ESMPs
FROM ESM TRAINING
Notes: Consider Underdrains When:
Wet Ditches, Banks, Spots in Road
Dry Bank and Remove Lubrication
Consider an Underdrain when you see perpetually wet ditches and banks along the road. They can even be installed under the cartway to dry out problem wet spots. When you dry out wet ditches and drain wet banks, you remove lubrication from the equation and make your banks more stable.

## Slide 23
When NOT TO USE:
For stormwater runoff.
Where surface runoff has not been addressed.
As storm sewer systems to convey surface runoff.
Underdrains
Road Base: ESMPs
FROM ESM TRAINING
Notes: Consider Underdrains When:
Wet Ditches, Banks, Spots in Road
Dry Bank and Remove Lubrication
Consider an Underdrain when you see perpetually wet ditches and banks along the road. They can even be installed under the cartway to dry out problem wet spots. When you dry out wet ditches and drain wet banks, you remove lubrication from the equation and make your banks more stable.

## Slide 24
Lack of Outlets / Long Runs
Underdrains
Notes: Project A

## Slide 25
Not for Surface Water Runoff!
Underdrains are not Storm Sewer Systems
Lack of Outlets / Long Runs
If ditch stabilization is needed ensure that rock lining is large enough to stay in place.
Underdrains
Notes: Consider Underdrains When:
Wet Ditches, Banks, Spots in Road
Dry Bank and Remove Lubrication
Consider an Underdrain when you see perpetually wet ditches and banks along the road. They can even be installed under the cartway to dry out problem wet spots. When you dry out wet ditches and drain wet banks, you remove lubrication from the equation and make your banks more stable.

## Slide 26
Underdrains
If ditch stabilization is needed ensure that rock lining is large enough to stay in place.
Large rock to prevent erosion.
Ditch shape was maintained.
Notes: Project D

## Slide 27
Why are underdrains not suitable for storm water?
Underdrains
Notes: Project A

## Slide 28
Underdrains
Notes: Project A

## Slide 29
Lack of Ditch Outlets.
AASHTO #1 is not riprap.
Utilize riprap if needed.
Surface runoff can expose underdrains.
Underdrains
Notes: Project A

## Slide 30
Sediment can close off underdrain & shorten effective life span.
Underdrains
Notes: Consider Underdrains When:
Wet Ditches, Banks, Spots in Road
Dry Bank and Remove Lubrication
Consider an Underdrain when you see perpetually wet ditches and banks along the road. They can even be installed under the cartway to dry out problem wet spots. When you dry out wet ditches and drain wet banks, you remove lubrication from the equation and make your banks more stable.

## Slide 31
Maintain ditch shape and capacity over underdrains.
Underdrains
Notes: Consider Underdrains When:
Wet Ditches, Banks, Spots in Road
Dry Bank and Remove Lubrication
Consider an Underdrain when you see perpetually wet ditches and banks along the road. They can even be installed under the cartway to dry out problem wet spots. When you dry out wet ditches and drain wet banks, you remove lubrication from the equation and make your banks more stable.

## Slide 32
UNDERDRAINS ARE NOT STORM SEWER SYSTEMS!
Use underdrains to address groundwater.
Use ditch and/or storm sewers to capture and convey storm water runoff.
Maintain ditch shape and capacity to convey stormwater flows.
If adequate outlets are not available, then evaluate use of storm sewer systems and/or rock lined ditches.
Underdrains
Notes: Consider Underdrains When:
Wet Ditches, Banks, Spots in Road
Dry Bank and Remove Lubrication
Consider an Underdrain when you see perpetually wet ditches and banks along the road. They can even be installed under the cartway to dry out problem wet spots. When you dry out wet ditches and drain wet banks, you remove lubrication from the equation and make your banks more stable.

## Slide 33
Underdrain, Storm Sewer
& Infiltration
LVR Overview
Underdrains
Storm Sewer
Infiltration – Structural BMPs

## Slide 34
Storm Sewer
Surface drainage patterns
Sub-surface drainage patterns
Existing Conditions - residential
Notes: Project C

## Slide 35
Storm Sewer
Surface drainage patterns
Sub-surface drainage patterns
Detention basin or other stable outlet
Add storm sewer
Notes: Project C

## Slide 36
Storm Sewer
Considerations:
Will the storm sewer reduce sediment impacts?
Consider when:
  Outlet opportunities are limited.
  Ditches are unstable due to excessive runoff.
  Open ditches or cross pipes are not feasible in residential or urban settings.
Consider grass swales over storm sewers.
Where will the system outlet?
How will the outlet location be stabilized?
Notes: Project C

## Slide 37
37
Montgomery County
Webber Road
$24,000 Grant, $2,000 in kind
Problems:
Excessive surface flow
Nowhere to outlet water
Practices Used:
Small storm sewer
Widened grass-lines swale
BEFORE
PROJECT SPOTLIGHT
Webber Road, Montgomery County
Notes: Best example of the three – flows

## Slide 38
2016 LVR Project
Montgomery County, Webber Road
$24K Spent, $2K in kind
ESMs Used:
Small storm sewer
Widened grass-lined swale
BEFORE
Constant ditch washouts, erosion into yards
PROJECT SPOTLIGHT
Webber Road, Montgomery County

## Slide 39
2016 LVR Project
Montgomery County, Webber Road
$24K Spent, $2K in kind
ESMs Used:
Small storm sewer
Widened grass-lined swale
BEFORE
Yards drain to road.
Nowhere to outlet water
PROJECT SPOTLIGHT
Webber Road, Montgomery County

## Slide 40
Constant ditch washouts, erosion into yards
2016 LVR Project
Montgomery County, Webber Road
$24K Spent, $2K in kind
ESMs Used:
Small storm sewer
Widened grass-lined swale
BEFORE
PROJECT SPOTLIGHT
Webber Road, Montgomery County

## Slide 41
From Grant Application
PROJECT SPOTLIGHT
Webber Road, Montgomery County

## Slide 42
2016 LVR Project
Montgomery County, Webber Road
$24K Spent, $2K in kind
ESMs Used:
Small storm sewer
Widened grass-lined swale
AFTER
Short storm sewer
Widened grass swale
PROJECT SPOTLIGHT
Webber Road, Montgomery County

## Slide 43
Short storm sewer
Widened grass swale
2016 LVR Project
Montgomery County, Webber Road
$24K Spent, $2K in kind
ESMs Used:
Small storm sewer
Widened grass-lined swale
AFTER
Webber Road, Montgomery County
PROJECT SPOTLIGHT
Webber Road, Montgomery County

## Slide 44
Short storm sewer
Widened grass swale
2016 LVR Project
Montgomery County, Webber Road
$24K Spent, $2K in kind
ESMs Used:
Small storm sewer
Widened grass-lined swale
AFTER
PROJECT SPOTLIGHT
Webber Road, Montgomery County

## Slide 45
Off-ROW drainage to storm sewer
Widened grass swale
2016 LVR Project
Montgomery County, Webber Road
$24K Spent, $2K in kind
ESMs Used:
Small storm sewer
Widened grass-lined swale
AFTER
PROJECT SPOTLIGHT
Webber Road, Montgomery County

## Slide 46
Short storm sewer
Widened grass swale
2016 LVR Project
Montgomery County, Webber Road
$24K Spent, $2K in kind
ESMs Used:
Small storm sewer
Widened grass-lined swale
AFTER
PROJECT SPOTLIGHT
Webber Road, Montgomery County

## Slide 47
Constant ditch washouts, erosion into yards
2016 LVR Project
Montgomery County, Webber Road
$24K Spent, $2K in kind
ESMs Used:
Small storm sewer
Widened grass-lined swale
BEFORE
AFTER
2016 LVR Project
Montgomery County, Webber Road
$24K Spent, $2K in kind
ESMs Used:
Small storm sewer
Widened grass-lined swale
PROJECT SPOTLIGHT
Webber Road, Montgomery County

## Slide 48
48
Pike County
Bartleson Road
$99,000 Grant, $17,000 in kind
Problems:
Excessive surface flow from small development
Flow erodes roadside ditch
Flow enters stream at bottom of hill.
Practices Used:
Storm Sewer
Energy Dissipater at Outlets
Reduce Flow Lengths
After
PROJECT SPOTLIGHT
Bartleson Road, Pike County
Notes: Best example of the three – flows

## Slide 49
49
Before
PROJECT SPOTLIGHT
Bartleson Road, Pike County
Constant ditch washouts, erosion into yards
Notes: Best example of the three – flows

## Slide 50
50
Before
PROJECT SPOTLIGHT
Bartleson Road, Pike County
Existing pipe outlet was unstable and required constant maintenance.
Notes: Best example of the three – flows

## Slide 51
51
Before
PROJECT SPOTLIGHT
Bartleson Road, Pike County
Ditch drained directly to stream.
Notes: Best example of the three – flows

## Slide 52
52
After
PROJECT SPOTLIGHT
Bartleson Road, Pike County
Inlet boxes located at intersection to capture flow.
Notes: Best example of the three – flows

## Slide 53
53
After
PROJECT SPOTLIGHT
Bartleson Road, Pike County
Multiple inlets & cross pipes to reduce flow lengths & break up flow volumes at
Notes: Best example of the three – flows

## Slide 54
54
After
PROJECT SPOTLIGHT
Bartleson Road, Pike County
A total of 4 separate “teardrop” basins were constructed for the outlets of 5 different pipes.
Notes: Best example of the three – flows

## Slide 55
55
After
PROJECT SPOTLIGHT
Bartleson Road, Pike County
A total of 4 separate “teardrop” basins were constructed for the outlets of 5 different pipes.
Notes: Best example of the three – flows

## Slide 56
Introduction
Underdrain
  Carries groundwater underground
  Outlets on surface
Storm sewer
  Carries surface water underground
  Outlets on surface

## Slide 57
What if groundwater impacts where you want to install storm sewer?
Can surface and groundwater be separated?
Underdrains can be installed in conjunction with Storm Sewers.
  Install underdrain to address groundwater issues and install storm sewer to convey storm water.
Seek as many outlets as possible and ensure outlets are stabilized.
Perforated storm sewer can collect both surface and groundwater.
  Use and installation based on project goals
    Infiltration vs. Capture
Storm Sewer

## Slide 58
CONSIDERATIONS for perforated storm sewer:
  Size appropriately for the volume of water being carried.
  Bed/backfill in clean stone .
  Wrap pipe and stone in non-woven geotextile fabric.
  Consider perforated inlet boxes for infiltration projects.
Storm Sewer

## Slide 59
Storm Sewer
Notes: Talk to manufacturers about perforated inlet boxes

## Slide 60
LVR Overview
Underdrains
Storm Sewer
Infiltration – Structural BMPs
Underdrain, Storm Sewer
& Infiltration

## Slide 61
Infiltration - Water moving downward into the space between soil particles.
  Structural infiltration BMPs can be used when storm water is collected and conveyed to a single location.
Infiltration
Notes: https://eschooltoday.com/learn/infiltration/

## Slide 62
Site Evaluation
Soil Type(s) – soil mapping, wetlands, drainage
Slopes
Hydrology, Drainage Patterns
Buildings
Aerial Photographs
  Area evaluation
  Is the site suitable
  for infiltration???
Infiltration
Notes: Project C

## Slide 63
Infiltration
Infiltration Design
Size based upon infiltration rate
Structure design should include the following:
  Level Bottom
  Uncompacted Bottom / Amended Soils
  Limit Water Depth
  Drawdown time
  Positive Overflow
  Flow path:
    Will flow re-concentrate?
    Is permission required for discharge?
Notes: Project C

## Slide 64
Infiltration Basins
Infiltration
Notes: Project B. infiltration/detention basin designed by engineer

## Slide 65
Infiltration
Rain Garden
Notes: Project C

## Slide 66
Infiltration
Rain Garden
Notes: Project C

## Slide 67
Infiltration
Rain Garden Basins
Notes: Project C

## Slide 68
Infiltration
Bioretention Swales
Notes: Project C

## Slide 69
Infiltration
Infiltration Sump
Notes: Project C

## Slide 70
3’ Deep, filled w/ R4 and edged with pallet stone.
Infiltration Sump
Infiltration
Notes: Project C

## Slide 71
71
BEFORE
PROJECT SPOTLIGHT
Dauphin County
Penbrook Borough
31st Street
$93,019 Spent, $10,126 In-Kind
Problems:
2.8 ac. drainage enters alley
Failed storm inlets
Eroding roadway & outlet
Discharges to Spring Creek
Practices Used:
Infiltration
Retention
Stabilized outlet

## Slide 72
31st & Charles Street, Penbrook Borough
Project Site

## Slide 81
Infiltration
When NOT to use infiltration practices:
  When site conditions limit infiltration:
    Clay soils
    Shallow Bedrock
    Saturated soils – spring seeps, wetlands, etc.
    Houses, septic systems, utilities may be impacted.
    Infiltration in the upslope ditch may saturate road base
  When no one can maintain the practice.
  If the practice will be outside the right-of-way and:
    Written permission is not obtained.
    Off-ROW practices that are 35% or more of the project cost or 500+ ft outside the ROW require SCC permission
Notes: Project C

## Slide 82
Summary
Underdrain
  Carries: groundwater
  Requires: slope/fall to carry water
  Outlets: on the surface
Storm sewer
  Carries: surface water underground
  Requires: slope/fall to carry water
  Outlets: on the surface
Infiltration practices
  Carries: surface water underground
  Requires: flat bottom and correct site conditions to achieve infiltration
  Outlets: underground via infiltration
    With a surface overflow
Notes: Project C

## Slide 83
Summary
Technical Bulletin: Underdrains, Storm Sewers & Infiltration
Compares Underdrain vs. Storm Sewers & Infiltration
https://dirtandgravel.psu.edu/general-resources/technical-bulletins/
Notes: Project C

## Slide 84
Summary
Technical Bulletin: Underdrains
Underdrain construction
https://dirtandgravel.psu.edu/general-resources/technical-bulletins/
Notes: Project C

## Slide 85
Questions? Discussion?

## Slide 86
DGLVR Program
Spending Update/ASR Refresher
  5-Year Spending Update
    All funding from agreement must be spent out by 6/30/24
    Current CD Status as of 2/13/2024
      Spent everything: 23 DGR, 20 LVR
      Committed everything: 24 DGR, 29 LVR
      Not committed: 17 DGR, 17 LVR

## Slide 87
DGLVR Program
Spending Update/ASR Refresher
  5-Year Spending Update - Financials
    Dirt and Gravel
      Committed: $4,279,904.22
      Not Committed: $484,442.34
    Low Volume
      Committed: $2,842,816.66
      Not Committed: $867,122.70
    Total
      DGR: $4,764,346.56
      LVR: $3,709,939.36
      Total: $8,474,285.92

## Slide 88
  Question:
  How do I know how much I need to spend to meet my spending requirements?
    Answer:
  This information is available in the GIS.
DGLVR Program
Spending Update/ASR Refresher

## Slide 89
  Question:
  How do I know if I have all my “old money” contracted?
    Answer:
  If your Committed Remaining is greater than the Balance Remaining.
DGLVR Program
Spending Update/ASR Refresher

## Slide 90
  Question:
  How do I know if I still have “old money” to contract?
    Answer:
  If your Committed Remaining is less than the Balance Remaining.
DGLVR Program
Spending Update/ASR Refresher

## Slide 91
DGLVR Program
Spending Update/ASR Refresher
  5-Year Spending Update
    If you are Green in both DGR and LVR, great job!
    If you are Yellow or Red in DGR and/or LVR, expect follow-up status calls/emails.